# System Test Report

| Test Set/Case Definition | Results | Expected Results | Comment/Issue |
| --- | --- | --- | --- |
| IBED RC3 Installation |  |  |  |
| Executing install script to install the IBED release. | Pass | After installing, either reboot the node or start the service. 'lsmod' will show all the loaded modules. | . |
| Mellanox OpenIB tests |  |  |  |
| Gen2 Basic Tests |  |  |  |
| open close HCA | Pass |  |  |
| ibv_get_device_guid | Pass |  |  |
| ibv_query_device | Pass |  |  |
| query legal ports | Pass |  |  |
| query illegal ports | Pass |  |  |
| query gid table with legal port and legal gid table idx | Pass |  |  |
| query gid table with legal port and illegal gid table idx | Pass |  |  |
| query gid table with illegal port and illegal gid table idx | Pass |  |  |
| create many ibv_devices | Pass |  |  |
| Mem Lock Check Tests |  |  |  |
| mem lock test | Pass |  |  |
| fork master | Pass |  |  |
| allocator | Pass |  |  |
| Multicast Tests |  |  |  |
| Multicast Test | Pass |  |  |
| QP Tests |  |  |  |
| qp tests | Pass |  |  |
| Resource Tracking Tests |  |  |  |
| resource tracking test | Conditional Pass |  | Fails for MR_TYPE = SHARE_MEMORY and LAST_BLOCK |
| IPoIB Tests |  |  |  |
| Ping tests using ib0 interface | Pass |  |  |
| Ping tests using ib1 interface | Fail |  | Self ping is successful but ping to other side is failing. See PR #33. |
| Ping resumes after down/up the interface | Pass |  |  |
| Ssh resumes after down/up the interface | Pass |  |  |
| Netperf Test using default packet size | Pass |  | Throughput = 1.14 Gbps |
| Netperf test using small packet size (256 bytes) | Pass |  | Throughput = 0.39 Gbps |
| Netperf Test using large packet size (1000000 bytes) | Pass |  | Throughput = 1.17 Gbps |
| Netperf Test overnight run | Pass |  | Throughput = 1.16 Gbps |
| SDP Tests | Fail |  | SDP is not stable in RC3 |
| RDS Tests | Fail |  | RDS is not supported. |
| SRP Tests | Fail |  | SRP is not supported |