OFED 1.2-beta1 SRP Initiator and Target Performance Test Report

- Test Summary

  - Using Oracle Orion IO performance test tool

    - On initiator, the OFED 1.1 SRP initiator has better IO performance than OFED 1.2 SRP initiator.

- OFED 1.1 initiator has maximum throughput 350MB/Sec on large sequential write and 410MB/Sec on large sequential read.

- OFED 1.2 initiator has maximum throughput 159MB/Sec on large sequential write and 318MB/Sec on large sequential read.

    - On target, the IBGD-1.8.3 SRP target has better IO performance on sequential write and OFED 1.2 SRP target has better IO performance on sequential read.

- IBGD-1.8.3 target has maximum throughput 181MB/Sec on large sequential write and 235MB/Sec on large sequential read.

- OFED 1.2 target has maximum throughput 159MB/S on large sequential write and 318MB/Sec on large sequential read.

  - Using in house test tool, mwb, testing on target, the IBGD-1.8.3 SRP target has better IO performance than OFED 1.2 SRP target.

- An average of 327 MB/sec throughput was achieved by using synchronous write, direct IO on IBGD and 227 MB/sec on OFED.

- When target array is almost full, the performance dropped by 0.6% on IBGD target and 2.2% on OFED target.

- Test Configurations

  - Initiator:

    - SLES 10 x86_64, Mellanox HCA-MT25208 (MT_0150000001), OFED 1.2-beta1.

    - RH4U4 x86_64, Mellanox HCA-MT25208 (MT_0150000001), OFED 1.2-beta1.

  - Target:

    - SLES 10 x86_64, Mellanox HCA-MT25208 (MT_00A0010001), SCST driver 0.96, SRP target driver, OFED 1.2-beta1, 8 74GB SATA hard drives, RAID5 (Areca 1220 controller), XFS filesystem.

    - SLES 10 x86_64, Mellanox HCA-MT25208 (MT_00A0010001), SCST driver 0.96, SRP target driver, OFED 1.2-beta1, 8 74GB SATA hard drives, Pass Through (Areca 1220 controller).

- Test Results

  - There were a total of 57 SRP system test cases including IO stress test, Ibnet and SRP target discovery, SRP connections, IB functionalities, IPoIB tests and IO performance tests.

  - Issues found on OFED 1.2-beta1 initiator:

    - Missing dnotify file under /usr/local/ofed/bin when running “start_srp_dnoity.sh”

sfw1:/usr/local/ofed/sbin # ./start_srp_dnotify.sh

/usr/local/ofed/sbin/srp_dnotify: line 32: /usr/local/ofed/sbin/../bin/dnotify: No such file or directory

    - Ib-bond:

      - Missing ib-bond on RH4U4 x86_64 under /usr/local/ofed/bin.

      - Write Error on sles10 x86 and sles10 x86_64:

test6:/usr/local/ofed/bin # ./ib-bond --bond-ip 192.168.1.199/255.255.255.0 --slaves ib0,ib1 --miimon 100 -v

enslaving ib0

./ib-bond: line 66: echo: write error: Operation not permitted

enslaving ib1

./ib-bond: line 66: echo: write error: Operation not permitted

bonding is up: 192.168.1.199

bond0: 00:00:00:00:00:00 192.168.1.199/24

      - Not able to bring up multipath devices.  Need to provide documentation to setup the environment.

  - Issues on OFED 1.2 SRP target:

    - Initiator lost a connection to target HCA port1 after adding a connection to target HCA port2.

    - OFED based SRP target is often to cause “ib_srp connection failed” on initiator.

- Test Tools

  - Using in house test tool, mwb, to perform synchronous write on IBGD and OFED targets with RAID 5.

  - Using Oracle Orion (Oracle I/O Numbers Calibration Tool) to perform read and write on OFED 1.1 and 1.2 initiators; and IBGD and OFED targets with raw devices.

- Performance Data

Figure1:

- Using mwb to performe synchronous write, direct IO from SRP initiator to the SRP target with 32 writes and 32 MB chunk.  Target has 8 74MB, 10K rpm hard drives on RAID 5 under Areca 1220 controller.

- An average of 327 MB/sec throughput was achieved by using synchronous write, direct IO on IBGD and 227 MB/sec on OFED.

- When target array is almost full, the performance dropped by 0.6% on IBGD target and 2.2% on OFED target.

- Notes

  - Ofed 1.1 - ofedsrpt: IOs run on ofed 1.1 initiator with ofed 1.2 target.

  - Ofed 1.1 - ibgd183: IOs run on ofed 1.1 initiator with ibgd1.8.3-rc16 target.

  - Ofed 1.2srpt: IOs run on ofed 1.2 target locally.

  - Ibgd183srpt: IOs run on ibgd183-rc16 target locally

Figure-2: Using Oracle Orion to perform IO on 8 raw devices on target (8 hard drives at Pass Through mode under areca 1220 controller).  The following is the throughput comparison between OFED 1.1 and 1.2-beta1 SRP initiators with OFED 1.2 SRP target.

Figure-2.a and 2.b: Large (1024KB) and small sequential reads (8KB)

- OFED 1.2 initiator (sles10) has maximum throughput 318MB/Sec on large sequential read.

- OFED 1.2 initiator (rh4u4) has maximum throughput 316MB/Sec on large sequential read.

- OFED 1.1 initiator (sles10) has maximum throughput 410MB/Sec on large sequential read.

- OFED 1.2 initiator (sles10) has maximum throughput 118MB/Sec on small sequential read.

- OFED 1.2 initiator (rh4u4) has maximum throughput 117MB/Sec on small sequential read.

- OFED 1.1 initiator (sles10) has maximum throughput 744MB/Sec on small sequential read.

- Notes:

  - Sles10-ofed1.2B: IOs run on ofed 1.2 under sles10 initiator.

  - Rh4u4-ofed1.2B: IOs run on ofed 1.2 under redhat 4 update4 initiator.

  - Sles10-ofed1.1: IOs run on ofed 1.1 under sles10 initiator.

Figure-2.c and 2.d: Large (1024KB) and small sequential writes (8KB)

- OFED 1.2 initiator (sles10) has maximum throughput 159MB/Sec on large sequential write.

- OFED 1.2 initiator (rh4u4) has maximum throughput 159MB/Sec on large sequential write.

- OFED 1.1 initiator (sles10) has maximum throughput 350MB/Sec on large sequential write.

- OFED 1.2 initiator (sles10) has maximum throughput 879MB/Sec on small sequential write.

- OFED 1.2 initiator (rh4u4) has maximum throughput 885MB/Sec on small sequential write.

- OFED 1.1 initiator (sles10) has maximum throughput 860MB/Sec on small sequential write.

- Notes:

  - Sles10-ofed1.2B: IOs run on initiator with target ofed 1.2 under sles10 initiator.

  - Rh4u4-ofed1.2B: IOs run on ofed 1.2 under redhat 4 update4 initiator.

  - Sles10-ofed1.1: IOs run on ofed 1.1 under sles10 initiator.

Figure-3: Orion – Performed IO on 8 raw devices on target (8 hard drives at Pass Through mode under areca 1220 controller).  The following is the throughput comparison between OFED 1.2-beta1 and IBGD-1.8.3-rc16 SRP targets with OFED 1.2-beta1 SRP initiator under Sles10.

Figure-3.a and 3.b: Large (1024KB) and small sequential reads (8KB)

- OFED 1.2 target (slel10) has maximum throughput 318MB/Sec on large sequential read.

- IBGD-1.8.3 target (rh4u3) has maximum throughput 235MB/Sec on large sequential read.

- OFED 1.2 target (slel10) has maximum throughput 118MB/Sec on small sequential read.

- IBGD-1.8.3 target (rh4u3) has maximum throughput 118MB/Sec on small sequential read.

- Notes:

  - Ofed1.2-target: IOs run on initiator with ofed 1.2 target.

  - Ibgd183-target: IOs run on initiator with ibgd-1.8.3 target.

Figure-3.c and 2.d: Large (1024KB) and small sequential writes (8KB)

- OFED 1.2 target (slel10) has maximum throughput 159MB/Sec on large sequential write.

- IBGD-1.8.3 target (rh4u3) has maximum throughput 181MB/Sec on large sequential write.

- OFED 1.2 target (slel10) has maximum throughput 879 MB/Sec on small sequential write.

- IBGD-1.8.3 target (rh4u3) has maximum throughput 880 MB/Sec on small sequential write.

- Notes:

  - Ofed1.2-target: IOs run on initiator with ofed 1.2 target.

  - Ibgd183-target: IOs run on initiator with ibgd-1.8.3 target.