## Slide 1: OFA NVMe Driver 2012 Release Plans
Q2
Q4
Q1
Q3
Release 1:
Initial Release
NVME 1.0b
Win7,2008R2
Release 1.1:
NVME Spec Updates
Public IOCTLs
Win8 Storport Specific
Bug Fixes
Win7,2008R2,Win8
Releases are binaries for x86, x64, matching source available on OFS via SVN.

## Slide 2: Release/Patch Criteria
Reviews
  Patches submitted by anyone, email to distribution list
  Patch submission should include time sensitivity/expectations
  Patch submission should include justification for the patch (what value will it add, and are tradeoffs what are they and why would we want to take a hit). If multiple implementation options were considered, what data/reasoning was behind the implementation choice.
  At a minimum reviews need to be competed by Intel, IDT and LSI representative
  Reviews include compliance with coding guidelines (in SVN) as well as logic
Testing
  All patches and release candidates required, at a minimum, the following;
    1 hour of data integrity testing using sdstress (Microsoft Tool)
    1 hour of heavy stress testing using IOMETER covering, at least, 512B, 4KB and 128KB ranging from 1 OIO to 64 OIO both sequential and random
    Quick and slow format of both MBR and GPT partitioning
    Microsoft SCSI Compliance, no failures except (warnings OK):
      READ_CAP due to the test support of a lower SBC than we do
      WRITE(10) due to what appears to be a false positive (investigating)
    Performance regression (scripts and procedures) are TBD; will be added shortly.
  Additional testing with other tools is encouraged
  Occurs in all supported OSs for the release
  Minimum test platform is latest QEMU. Those with their HW should test on it as well. QEMU is available at https://github.com/nvmeqemu/nvmeqemu