## Slide 1: Remote Persistent Memory Think Tank
Report Out
Prepared by a cast of thousands
April 13, 2018

## Slide 2: Think tank abstract
Challenge - Some people think that Remote Persistent Memory over Fabrics is the Next Big Deal. But is it really? If it is, what is needed to get it off the ground and to drive adoption?
Abstract – There has been a lot of buzz in the industry over the last few years related to Persistent Memory but much of that buzz has been associated with local Persistent Memory. There have been efforts to get a discussion about remote PM off the ground, but so far they have been relatively isolated efforts. This Think Tank is focused on a) understanding if there is interest in remote persistent memory, and b) if so, what is needed to get the effort moving.

## Slide 3: process  assignment
Identify enough use cases for remote PM to decide if there is adequate motivation to move forward
Identify current obstacles
Define the missing/incomplete elements that are required to enable rapid/broad adoption of remote PM
Identify appropriate forums needed to overcome those obstacles

## Slide 4: Executive summary
Big Deal? Yes, but within reason. Much work remains to quantify and demonstrate a crisp value proposition.
  “There’s a pony in here somewhere”
Use Cases – we focused on a couple, but there’s quite a list more generally. The list needs to be explored more deeply.
Current Obstacles – Yes 
What’s Required to Get It Going – A few items were identified, there are more
Process –
  Refine the list of use cases and identify more
  Identify common characteristics among them
Appropriate Forums – Use the new SNIA/OFA Work Register. Begin meeting the context of OFIWG, since OFA is entirely open source

## Slide 5: an important caution
We need to be very careful to keep the API requirements pure, and distinct from the characteristics of any given implemention
To do that, we will focus on:
What does the use case demand?
Why does the use case demand it?
X How does the programming model provide that function?
We will steer clear of mechanisms

## Slide 6: some random observations
Interesting thought: Think of RPM in terms of non-uniform memory
  accesses to RPM vs LPM are by definition NUMA
  stage accesses from RPM to either local DRAM or local PM
  Assumption of non-uniform memory  may be more flexible, has more attributes
Persistent memory devices have two distinct attributes:
  High density / capacity compared to DRAM (and at lower power compared to DRAM)
  Persistence
Some usages may value one over the other
  e.g. Dreamworks. persistence is valuable, but the Dreamworks usage is driven by the availability of large capacity, shared database.
  The database is Read Mostly, Write Infrequently
  Programming model for use cases that don’t depend on persistence may be significantly easier

## Slide 7: Some random observations
Persistence Memory is neither memory nor storage. It is a new layer in the memory hierarchy
Not all usages assume cached data
  e.g. Put/Get operations are non-cached
   a cache flush/commit semantic may not be needed in all RPM use cases

## Slide 8: Checkpoint restart
Problem: Checkpointing of a large machine can consume a significant fraction of the available compute time.
In the limit, a machine spends all its time checkpointing and does not make forward progress on the application
Checkpointing today is typically done to a burst buffer and then spooled off to Lustre in the background
Objective – spend less time checkpointing and more time computing
Two possible approaches:
Accelerate the existing paradigm by viewing RPM as an exquisitely fast and large burst buffer
Write a new stack based on an HA model – nontrivial

## Slide 9: Dreamworks – the 8 sec problem
Currently each animator works with only a few seconds of an animated movie
Typically, he cannot see most of the rest of the movie
Objectives
  Enough fabric attached memory to contain the entire movie
  Accessible by all animators
If it’s PM, it fits more neatly into a memory hierarchy than a storage hierarchy

## Slide 10: machine learning
Characteristic workloads tend to be 80% random reads
Probably a poor fit for a sequential storage device

## Slide 11: Streaming sensor data use case
Use case: Capturing data streaming from a sensor array
Performance solutions today are small and expensive
Capacity solutions may not be high enough performance

## Slide 12: Will developers adopt it?
In the absence of a killer app, adoption of will be a function of:
  Price
  Capacity
  Persistence
  Performance
Example: there are multiple ways to achieve high capacity
  RPM might be adopted if the price / capacity is reasonable
A killer app is one where the introduction of RPM enables functionality that is not possible today
  There are no killer apps (yet)
The checkpoint/restart problem may become a killer app
Ira’s killer app: Parallel address space, treating as memory not suffering DRAM cache misses. Eg: PGAS

## Slide 13: What’s Missing?
Global addressability
Synchronization mechanisms
  multiple instances of an application must block until data has reached a persistent state
What is the availability model in the face of power failure?
  Power fail atomics
Data validation problem – no way to know if data arrives on the persistent media intact
  Same problem with storage today
What is equivalent of pcommit and remote PM?
No use cases for pcommit

## Slide 14: Consolidated use cases - caveats
Liberal enumeration with some attempt at application relevant framing
Overlaps information on earlier slides (cross-referenced)
Tried to omit technology-only statements, although some descriptions are technology centric. At least hint at “why” with some “what” and no “how”.
Some use cases may overlap or be relevant when used together

## Slide 15: Consolidated use case list
Local copy centric – data is copied from remote PM to local DRAM or PM for caching and/or manipulation, then copied back as needed
Immediate high availability - Local access to PM + remote access for HA for data recovery and failover with little to no work loss (slide 3 above)
HPC Checkpoint/Restart – Application pauses to enable rapid copy of relevant state to a checkpoint. Recovery can reference a recent checkpoint. Job suspend/resume references most recent checkpoint. (slide 3 above)

## Slide 16: Consolidated use case list
Distributed collaboration – Remote PM provides a central repository for the recent work of a distributed team collaborating on a large artifact such a movie. Fragments being created by individuals can be quickly viewed locally in the surrounding context. (slide 4 above)
Random byte range read after ingest – Applications such as machine learning with workloads that are mostly short random reads by parallel threads after ingesting a large body of data. (slide 5 above)
Aggregated updates – Cache line accesses such as those comprising a transaction are aggregated for communication to remote PM for visibility and/or redundancy.

## Slide 17: Consolidated use case list
NUMA on Steroids – Extend and merge the concepts of NUMA, caching and tiering from CPU’s and storage to provide autonomous operation controlled by application informed allocation policies (slide 5 above)
Volatile memory expansion – Remote PM is used to expand volatile memory capacity with lower cost, higher density and larger (beyond local) scale than DRAM. (slide 5 above)
Mirrored transactions – Transactions using local PM are replicated in well know ways to local PM on other nodes. May or may not require remote access at the PM level.

## Slide 18: Consolidated use case list
GPU centric – Copy state directly between GPU memory and local or remote PM without going through DRAM.
Rehydration – Remote PM used for DB logs/checkpoints to enable rapid re-hydration of memory after failure. Cost is more aligned with large scale (e.g. SAP HANA) than scaled out open source (slide 6 above)
Metadata de-amplification – When metadata becomes larger than memory, metadata paging can cause read/write amplification relative to payload data read/write. PM density and remote PM scale can offset this type of amplification.

## Slide 19: consolidated gap list
Global addressability – means of identifying versioned data relevant to an application during restore (HA or checkpoint). Applicable to sharing as well?
Synchronization for weakened memory semantics – non cache coherent access (for recovery or sharing at scale) still requires a means of establishing weaker consistency appropriate to the application. Ordering barriers (as opposed to fine grain acknowledgement) may be one approach.
Power fail atomicity – different from current processor and network atomics, proving to have vexing subtleties
NIC persistence – Means of allowing network endpoints to participate in power fail atomicity.
Economics estimation - Tools for estimating and comparing economics of memory/storage hierarchies with and without (remote) PM
Evolved NUMA – enable use case 7 above.

## Slide 20: Backup slides and raw notes from our discussion

## Slide 21: What is PMoF?
Is this distributed file system or shared memory?
  Andy: Oracle exascale showed clients could access memory in remote server without impacting server CPU cycles.
How to create persistence? No flushing needed in future?

## Slide 22: use cases
HA usage – first among others. What’s driving the HA usage?
Identify early adopters or usages for PM.
How are these getting used?
Scale out – use case where PM has storage.
Fast resume-usage
What about Cost?
Scott Ashley – Assume its faster than flash, assume its byte addressable. There is no need for byte addressable  requires new S/W stack.
Use case for scott: Checkpoint restart.
  Why not use local PM? Requires S/W to refer to pointer in PM
  Could save the state then theoretically can refer to that state. Similar to VM pause and resume. Pause just before the the crash

## Slide 23: New SW Stack definition
On top of current HA usage? – Yes, HA is required.
  Replace Lustre
Acknowledging Checkpoint as a usage
Regular memory in 2 nodes works? We cannot use memory for storage; should be dedicated to computation
Why checkpoint on PM? Why doesn’t existing solutions work?
  Higher bandwidth, less time checkpointing, more time computing
If CPUs can support then it will be awesome
Local pooled memory  acts as shared memory. Eg: Dreamworks

## Slide 24: Machine Learning Usage
90% read and a lot of random access
Two kinds of PM
  Expensive than DRAM; doesn’t work for making copies
  Cheaper than DRAM
Assumption of non-uniform memory  may be more flexible, has more attributes
Could RPM be non-uniform memory
Two attributes for PM= Capability, persistence. Which are important?
  Both

## Slide 25
Persistence Memory is a new tier of memory.
SAP Hana solving the problem that their memory is now persistent
High bandwidth but capacity is pretty limited but cannot afford
At some point, capacity will be impacted when heuristics come into play
NVDIMM-T; mixed media in DIMM Form factor

## Slide 26: So is it a big deal?
100 of linux cheap boxes  still don’t know PM relevance in DBs
From DB POV don’t see case for RPM, may be cheaper if we use NVMe SSD for replication
Its interesting, another layer that is farther from local memory
Storage is easier to pool; what about pool of PM? Issue: cost & capacity
Front end is RPM but back end is different usages like battery backup

## Slide 27: Why aren’t developers developing apps?
Local PM accesses are enabled by JEDEC, Oses…
HA, price, density is relevant. Perf can be secondary
  Byte addressability is not an issue
  Lower latency, improved bandwidth works if price allows.
Ira’s killer app: Parallel address space, treating as memory not suffering DRAM cache misses. Eg: PGAS

## Slide 28: PM Role
Byte addressable PM is fast; what is the cost replicated? Because this is the limiting factor
Checkpoints can be done today but compute is sacrificed. Machine fails. Machine approx 20,000 cluster nodes (2S, IB)

## Slide 29: Big questions (during conclusion)
PM is here, well and alive. But Data center loses power then what happens? Who maintains state. …and restore
Univ of Santa Cruz  address PM so that it is globally available? – Project name Twizzler (LINK)
Can multiple LPMs work as RPM? Pre-fetch, NUMA idea…Full PM is somewhere else but some pieces of it is pre-fetched into LPM