## Slide 1
OFA OpenFabrics Interfaces Project
Data Storage/Data Access working group
February 2016
kfabric - kernel fabric interface
Direction Check with Linux Kernel Maintainers

## Slide 2: Objective (today)
Describe what we’re trying to accomplish, and its rationale
Describe the approach being taken
Ask for your feedback/direction check - Is this an acceptable direction that merits further development?

## Slide 3: kfabric objectives
Develop APIs to support kernel-based storage and remote data access
  filesystems, object I/O, block storage, persistent memory (emerging)
Network agnostic
  new network types should not require emulating an existing one
    device drivers are typically based on a specific network technology
Present a consumer-oriented network abstraction
Support for emerging use cases - NVM
  NVM for storage and for memory access – see upcoming slide
Support for emerging fabrics
  Allow for innovation with new networks as they emerge
Support for existing networks
  Must run over existing network technologies

## Slide 4: What we are proposing
Kfabric: an abstract, kernel mode API for I/O
  ‘Abstract’: the API is expressed in terms of I/O operations, not network protocols
  e.g. ‘read file’, ‘write file’ vs ‘post send request’
Requirements driven by emerging technologies
  New/emerging networks require a transport neutral, RMA-enabled API
  NVM devices and how they will be used
Demand exists for an abstract, message passing API based on RDMA

## Slide 5: Why a new kernel API?
Reliable sockets is a byte streaming interface
  semantics don’t map well to messaging operations
  kfabric complements sockets by providing a reliable message service
Kverbs is a low level device driver
  tied to the architecture of the underlying wire
  not suitable for some emerging fabrics
  kfabric is expected to call kverbs for certain networks
The semantics desired by current and emerging storage applications are not well addressed by current APIs

## Slide 6: Storage protocols
Block and object storage protocols do not map well to sockets
Reliable sockets are stream-oriented and require message markers
Datagram sockets map well to messages but at the expense of reliability
Sockets requires implicit buffering at the sender and receiver, which adds latency, increases CPU utilization, and reduces throughput
Socket’s completion semantics guarantee only that the data is buffered locally; there is no notion of reliable delivery
Sockets does not provide mechanisms for one-sided access (RMA)
  requires an active software agent on both the sender and receiver.
Socket connections don’t allow multiple thread access without external synchronization
  e.g. a mutex to ensure single thread access to partial messages and to avoid losing markers

## Slide 7: Storage protocols
Block and object storage protocols map well to reliable, message-based APIs that provide RMA services
kfabric provides reliable and unreliable message services
  processes do not need to maintain message markers
kfabric does not require implicit buffering
kfabric completion semantics are a semantic match with storage reqmts
  e.g. local completions, remote completions, ordered and out-of-order delivery…
kfabric endpoints are (selectably) thread-safe
  multiple threads can progress them independently
  serialization can be done by the provider, not by the application
kfabric provides one-sided semantics enabling direct hardware access without CPU intervention

## Slide 8: Emerging storage protocols
Present day storage protocols are usually asynchronous and based on a ‘server push’ model for reads and a ‘server pull’ model for writes
Byte-addressable NVM is likely to introduce a synchronous, client driven model
Implies a greater reliance on one-sided operations, which requires richer completion semantics
  e.g. remote completions, completions based on data placement…

## Slide 9: Emerging technology - NVM
Data replication is the main storage use case when it comes to “RDMA with NVM”
  Writing multiple copies of client data to multiple nodes
  All writes must reach durability point before signaling completion.
  Fabrics are not just limited to traditional Ethernet or IB
  Devices are not just limited to traditional RNIC or HCA
We need a framework to support
  Diverse providers w/o requiring emulating existing one.
  Richer completion semantics
  Multicast RDMA
  …

## Slide 10: Positioning kfabric in the kernel
We believe that kfabric is best positioned as a peer to the kernel TCP sockets stack
Rationale
  message orientation complements socket’s reliable stream orientation
  adds support for one-sided (RMA) operations
  adds support for asynchronous operations
  rich set of completion semantics is a good semantic match to storage application usage models

## Slide 11: kfabric, libfabric relationship
  kfabric
  is: kernel modules for storage and remote data access
  is not: the kernel component of libfabric
  libfabric
  a user-mode library for distributed and parallel computing
  may be leveraged for user mode storage or data access (tbd)
  libfabric access to kernel services are performed by the provider(s) using the provider’s kernel drivers
kfabric complements libfabric by filling out the OFI suite of APIs

## Slide 12: Support for NVM

## Slide 13: I/O stack including kfabric (similar diagram for user mode using libfabric)
kernel application
NVM
VFS / Block Layer
HBA
local block I/O
NVMe
SCSI
ulp*
NVM
local byte-addressable
ulp*
kverbs
HCA
NIC, RNIC
IB
RoCE, iWarp
SRP, iSER, NFSoRDMA, NVMe/F
remote byte-addressable
ulp*
NVM
mem bus
byte access
VFS / Block-based FS / Network FS
NIC
IP
iSCSI
remote block/file I/O
sockets
byte access
fabric
ulp* = expected future ULPs, kfabric* is intended as a single API regardless of local or remote and regardless of the wire.
kfabric*
kfabric*
provider
PCIe
provider
arbitrary fabric

## Slide 14: kfabric architecture

## Slide 15: kfabric Framework
kfabric API
Kfabric API
Kfabric Providers
Device Drivers
New Providers**
New Devices
kernel Verbs
iWarp
InfiniBand
RoCE
Verbs Provider
Red = new kernel components, ** = e.g. NVM
NIC
Kernel Sockets
Sockets Provider

## Slide 16: kfabric API – the details
kfabric interfaces form a cohesive set
and not simply a union of disjoint interfaces.
The interfaces are logically divided into two groups:
control interfaces: operations that provide access to local communication resources.
communication interfaces expose particular models of communication and fabric functionality, such as message queues, remote memory access, and atomic operations. Communication operations are associated with fabric endpoints.
kfabric applications typically use control interfaces to discover local capabilities and allocate resources. They then allocate and configure a communication endpoint to send and receive data, or perform other types of data transfers, with storage endpoints.

## Slide 17: kfabric API
Consumer APIs
kfi_getinfo() kfi_fabric() kfi_domain() kfi_endpoint() kfi_cq_open() kfi_ep_bind()
kfi_listen() kfi_accept() kfi_connect() kfi_send() kfi_recv() kfi_read() kfi_write()
kfi_cq_read() kfi_cq_sread() kfi_eq_read() kfi_eq_sread() kfi_close() …
Provider APIs
kfi_provider_register() During kfi provider module load a call to kfi_provider_register() supplies the kfi api with a dispatch vector for kfi_* calls.
kfi_provider_deregister() During kfi provider module unload/cleanup kfi_provider_deregister() destroys the kfi_* runtime linkage for the specific provider (ref counted).
kfabric API

## Slide 18: kfabric Naming
Repo naming – net/kfabric/ or drivers/kfabric/
API naming – kfi_*()
Module naming
  Framework: kfabric.ko
  Providers: kfi_xxx.ko
  Test: kfi_test_xxx.ko

## Slide 19: kfabric Repo Layout
kfabric
kfi (framework)
prov (providers)
include
tests
ibverbs
Sockets
ibverbs
sockets
Documentation
kfabric.c (kfi.c)
Makefile/kbuild
Others…

## Slide 20: Discussion

## Slide 21
Back-up

## Slide 22
OFI Backup Slides

## Slide 23: Background
OpenFabrics Interfaces project (OFI) created by OFA 8/2013
Charter - develop, test and distribute:
  An extensible, open source framework that provides access to high-performance fabric interfaces and services.
  Extensible, open source interfaces aligned with ULP and application needs for high-performance fabric services
In short, I/O stack(s) that maximize network consumer effectiveness
OFI currently comprises two working groups:
  OFI WG – user mode APIs for distributed and parallel computing
  Data Storage/Data Access WG – kernel and user mode APIs for storage and data access
Discussion today is solely about kernel mode APIs for storage and data access

## Slide 24: OFI Taxonomy
OFI created a taxonomy for “classes of consumers”
  objective is to focus on defining the requirements for each class
  two working groups launched to focus on the first two classes
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Msg passing
MPI middleware
Structured data
Unstructured data
Skts apps
IP apps
Shared memory
- PGAS
- languages (SHMEM, UPC…)
OFI WG
DS/DA WG
OpenFabrics Interfaces - OFI
Notes: This slide describes how the two working groups, DS/DA and OFI WG are each focused on its respective ‘class of application’.

## Slide 25: OFI – kfabric/libfabric
Libfabric Enabled Applications
libfabric
Communication Services
Connection Management
Address Vectors
Completion Services
Event Queues
Counters
Data Transfer Services
Message Queues
Tag Matching
RMA
Atomics
Control Services
Discovery
OFI Provider
Address Vectors
Event Queues
Counters
Message Queues
Tag Matching
RMA
Atomics
Discovery
Triggered Operations
Triggered Operations
MPI
SHMEM
PGAS
. . .
NIC
TX Command Queues
RX Command Queues
Connection Management

## Slide 26: kfabric Mission
Create network APIs to support kernel-based storage
  filesystems, object I/O, block storage
  Incorporate high performance storage interfaces
  Focus on emerging storage and memory technologies e.g. NVM
Transport independence, consumer portability
  Define an API which is not derived from a specific network technology
  Base the API on a higher level abstraction built on message passing semantics
Emphasis on performance and scalability
  Minimize code paths to device functionality for performance
  Focus on optimizing critical code paths
  Eliminate code branches from critical paths wherever possible
Smooth transition path to emerging fabrics and new use cases
  NVM as persistent memory
  NVM as persistent storage
  Independent of any particular network technology
Notes: DS/DA is responsible for APIs for both kernel and user storage access. Kfabric is for the kernel version.

## Slide 27
NVM Backup Slides

## Slide 28: Motivation
  NVM is of great interest to OFA members and consumers of OpenFabrics Software (OFS)
  NVM as persistent memory: access to remote PM via a network is unlike existing memory models and warrants further discussion
  NVM as storage: likely to have an impact on how storage is architected, deployed, and accessed to warrant a discussion of NVM for I/O, and an API to access it
  Both ‘Data Storage’ and ‘Data Access’ are therefore potentially impacted by the emergence of NVM

## Slide 29: Scope
NVM as a target of I/O operations
  out of scope: NVM as a target of memory L/S ops
Accessed as a local device
  attached to the local I/O bus or
  attached to a memory channel
Accessed as a remote device
  attached to a network

## Slide 30: NVM access methods summarized
Case | Access method |  | note
1 | local memory access | access via memory load/store ops | (1)
2 | local byte-level access | accessed as I/O | 
3 | local block access | general case of byte access | (2)
4 | remote byte-level access |  | 
5 | remote block access |  | 
Case 1 is out of scope for DS/DA but is included here for completeness
Block level access, where the target is described by an address and extent, is seen as the general case of byte-addressable memory, where the extent is as small as 1 byte.

## Slide 31: NVM local access models
DIMM
DIMM
DIMM
NV
DIMM
MC
fs
SSD
block access* via e.g. NVMe
memory (“PM”)
(out of scope)
MC
NV DIMM
NV DIMM
NV DIMM
NV
DIMM
I/O –
Kfabric anticipates that NVM devices will export a native byte-addressable interface
NVM devices today export a block interface (even if the underlying geometry is byte-addressable).
byte-addressable (kernel or user mode)
block (kernel mode only)
l/s
i/o

## Slide 32: NVM byte addressable accesses
SSD
NIC
NIC
I/O device exports a byte-addressable or block level I/O interface
SSD
NVM
shared remote access I/O device
NV DIMM
NV DIMM
NV DIMM
NV
DIMM
consumer
Consumers (clients) of NVM I/O include
file or object storage – user or kernel mode (Lustre, CEPH…)
block storage consumers – kernel mode (iSER, SRP, NVMef…)
byte level consumers - user or kernel mode (no ULPs defined yet…)
NV DIMM
NV DIMM
NV DIMM
NV
DIMM
CPU
CPU
NV
DIMM
Q: does a consumer distinguish between uniform memory accesses to NVM, (load/store, which are local only), and NUMA accesses to NVM (using an I/O paradigm, which may be local or remote)?

## Slide 33: NVM remote access model
CPU
SSD
NIC
NIC
CPU
I/O device exports a byte-addressable or block level I/O interface
SSD
NVM
shared remote access I/O device
NV DIMM
NV DIMM
NV DIMM
NV
DIMM
client
Consumers (clients) of NVM I/O include
user or kernel file or object storage (Lustre, CEPH…)
block storage consumers (iSER, SRP, NVMef…)
byte level consumers (no ULPs defined as of yet…)

## Slide 34: NVM – two main use cases
Storage – kernel and user mode accesses
  NVM accessed through a file system
    Block I/O, File I/O, Object I/O
  Via an I/O fabric e.g. PCIe using non-transparent bridging
  Via a network – Ethernet, IB, emerging
Persistent Memory – kernel and user mode accesses
  Memory semantics – load/store to local or remote persistent memory

## Slide 35: kfabric for NVM
Storage data mirroring use cases
  Direct memory-like access to local or remote NVM through:
    PCIe fabric – non-transparent bridging
    Ethernet fabric – Proprietary implementation
  Prefer one-sided / lightweight operation offered by kfabric
Storage block access use cases
  Direct block access to local or remote NVM
    PCIe fabric – NVMe devices already contain queues, no need to layer IB queues on top of those existing queues.
    kfabric does not begin from the perspective of a classical connection-oriented protocol
    e.g. NVM benefits a lighter weight connection protocol

## Slide 36
kfabric Architecture Backup Slides

## Slide 37: kfabric Provider
kfi_provider_register (uint version, struct kfi_provider *provider)
kfi_provider_deregister (struct kfi_provider *provider)
struct kfi_provider {
const char *name;
uint32_t version;
int (*getinfo)(uint32_t version, const char *node,
const int service, uint64_t flags,
struct fi_info *hints, struct kfi_info **info);
int (*freeinfo)(struct kfi_info *info);
int (*fabric)(struct kfi_fabric_attr *attr,
struct fid_fabric **fabric, void *context);
};

## Slide 38: kfabric Application Flow
Initialization
Server connection setup (if required)
Client connection setup (if required)
  Connection finalization (if required)
Data transfer
Shutdown

## Slide 39: kfabric Initialization
kfi_getinfo( &fi ) Acquire a list of desirable/available fabric providers.
Select appropriate fabric (traverse provider list).
kfi_fabric(fi, &fabric) Create a fabric instance based on fabric provider selection.
kfi_domain(fabric, fi, &domain) create a fabric access domain object.

## Slide 40: kfabric End Point setup
kfi_ep_open( domain, fi, &ep ) create a communications endpoint.
kfi_cq_open( domain, attr, &CQ ) create/open a Completion Queue.
kfi_ep_bind( ep, CQ, send/recv ) bind the CQ to an endpoint
kfi_enable( ep ) Enable end-point operation (e.g. QP->RTS).

## Slide 41: kfabric connection components
kfi_listen() listen for a connection request
kfi_bind() bind fabric address to an endpoint
kfi_accept() accept a connection request
kfi_connect() post an endpoint connection request
kfi_eq_sread() blocking read for connection events.
kfi_eq_error() retrieve connection error information

## Slide 42: kfabric Reliable Datagram Xfer
kfi_sendto() post a Reliable Datagram send request
kfi_recvfrom() post a Reliable Datagram receive request.
kfi_cq_sread() synchronous/blocking read CQ event(s).
kfi_cq_read() non-blocking read CQ event(s).
kfi_cq_error() retrieve data transfer error information
fi_close() close any kfi created object.

## Slide 43: kfabric message data xfer
  kfi_mr_reg( domain, &mr ) register a memory region
  kfi_close( mr ) release a registered memory region
  kfi_send( ep, buf, len, fi_mr_desc(mr), ctx ) post async send from memory request.
  kfi_recv( ep, buf, len, fi_mr_desc(mr), ctx ) post async read into memory request.
  kfi_sendmsg() post send using fi_msg (kvec + imm data).
  kfi_readmsg() post read using fi_msg (kvec + imm data).

## Slide 44: kfabric RDMA data transfer
kfi_write() post RDMA write.
kfi_read() post RDMA read.
kfi_writemsg() post RDMA write msg (kvec).
kfi_readmsg() post RDMA read msg (kvec).

## Slide 45: kfabric message data transfer
kfi_send() post send.
kfi_recv() post read.
kfi_sendmsg() post write msg (kvec + imData).
kfi_recvmsg() post read msg (kvec+ imData).
kfi_recvv(), kfi_sendv() post recv/send with kvec.