## Slide 1: Network Acceleration Smart NICs, fpga’s, switch Offloads, …
Sean Hefty
May 2019
Intel Corporation

## Slide 2: Endpoint Accelerators Smart NICs, FPGA’s, GPU’s

## Slide 3: Objectives
Support offloaded accelerations in conjunction with network
  Smart NIC, FPGA, GPU, enhanced switches
  Local and/or remote accelerations
  Inline and look-aside
Discover available network functions
Enable functions at specific points in network data flows
Expose common software APIs to apply data operations on network flows
This is NOT an FPGA development kit or a general API for executing on GPU kernels.

## Slide 4: Communication Acceleration API Requirements
Select accelerator and function
Support local and remote accelerations
Provide necessary input parameters and output results
Network protocol may need enhancements
SmartNIC SW may need to program function prior to use
Discovery mechanism – available vs active
Support long-running functions (out-of-band execution)
Persistent vs on-demand functions
SmartNIC
Compute Node
inline
lookaside
port
Network
SmartNIC
inline
lookaside
port
Processor core(s)
memory
storage
memory
storage
memory

## Slide 5: Proposed Vision of Solution
Open source communication framework
Hardware vendor specific implementation
Application driven APIs
Define mechanism to pass input/output parameters and invoke acceleration
Extend existing communication framework to support acceleration functions
APIs targeting application use of specific accelerations
Based on internal hardware prototyping

## Slide 6: Proposal (Work In Progress)
Introduce new provider capability
Extend attributes to request/report available accelerations
Introduce new OFI object that corresponds to an acceleration
  Network function
  Generic base definition
Specify network function with data transfers
  Apply to all transfers of a specific type
  Specify per operation

## Slide 7: Network Functions
New capability
#define FI_NETWORK_FUNC (1ULL << ?)
enum {
/* well known functions */
fi_nf_noop,
fi_nf_chain,
…,
/* OR in FI_PROV_SPECIFIC for
* vendor specific functions
*/
};
struct fi_nf_info {
struct fi_nf_info *next;
int type;
uint64_t caps;
uint64_t mode;
uint64_t flags;
void *data;
size_t data_len;
};
Define well-known functions, allow for extensions
  ‘Chain’ groups multiple functions together as a single larger function
Generic structure to request/report available functions
  Returned by existing fi_getinfo() call
  Extend domain attributes

## Slide 8: Network Functions
Open a network function
int fi_network_func(domain,
struct fi_nf_info *nf_info,
void * context,
uint64_t flags,
struct fid_nf **nf);
fi_ep_bind(ep, nf, flags);
e.g. flags = FI_SEND | FI_RECV
e.g. flags = FI_WRITE | FI_REMOTE_WRITE
e.g. flags = 0
Associate function with endpoint
  Support providers that must configure function and endpoint prior to use
  Can specify types of data transfers to apply function to
  Or indicate that function will be specified when submitting the data transfer

## Slide 9: Network Functions
Specify function to apply to the current data transfer via existing context parameters
  Provide any needed input/output parameters
struct fi_nf_context {
struct fid_nf *nf;
void **params;
size_t param_cnt;
size_t *param_len;
void *reserved[4];
};
struct fi_deferred_work { … }
fi_control(…)
FI_QUEUE_WORK
FI_SUBMIT_WORK
FI_CANCEL_WORK
FI_FLUSH_WORK
Re-use deferred work queues to execute long-running functions separate from current data transfer
  Assumes results will be used by future transfer(s)

## Slide 10: analysis
Supports discovery of local functions and available protocols
Handles setup of local hardware
  Synchronous calls to open network function and bind
Still need vendor specific structures and APIs
  Wraps framework
  Needed: common way to reference non-host memory not in VA space
Not handled: mechanism to allocate or configure remote accelerators
  Creating network function is synchronous call

## Slide 11: network Accelerators collective offloads, etc.

## Slide 12: introduction
Support fabric based offloads
  Versus NIC based offloads
Immediate goal: accelerate collective operations
  SmartNIC / FPGA proposal focuses on endpoint accelerations
  This proposal focuses on network accelerations
  Separation is purely for convenience of discussion and focus
Solution should not be limited to collectives
Avoid trying to turn OFI into MPI

## Slide 13: network Accelerators
Switch Accelerator Optimize distributed application communication
NIC
inline
lookaside
port
NIC
inline
lookaside
port
May work in conjunction or independently from NIC acceleration
NIC involvement in protocol likely, but not required

## Slide 14: Network accelerators
Invoked via protocol
  Endpoint acceleration may be invoked via protocol or SW APIs
Intercept and process select traffic
  Identify packets for processing based on application protocol fields
  May have dedicated protocol for accelerations
Input/output carried in message headers and data
May require full or partial fabric configuration
  Management outside scope of OFI

## Slide 15: Collective Analysis
Analyze specific collectives as examples
  Extract and generalize requirements
  Identify existing or new OFI constructs that could support operation
Top priority operations (based on literature review)
  HPC – All Reduce, Barrier, Broadcast
  AI – All Reduce, All to All, Reduce-Scatter, All Gather
Analyzing high-level requirements, not implementation

## Slide 16: Communication Groups
MPI_Comm_split(comm, color, key, &newcomm)
Conceptual operation:
  All members of comm join a new group ‘color’
  New ranks defined by key
MPI_Comm_free(comm)
MPI_Comm_dup(comm, &newcomm)
  Used to separate traffic for ‘private’ communication
Groups
  Ordered set of processes
  All processes must define groups the same
  Used to create new communicators

## Slide 17: Barrier
MPI_Barrier(comm)
Conceptual operation:
  Wait until all peers reach synchronization point
Simple OFI fit:
  Each rank sends message to each peer
  Each rank receives message from each peer
reliable multicast
counters

## Slide 18: BroadcasT
MPI_Bcast(&buffer, count, datatype, rank, comm)
Conceptual operation:
  Rank sends an array of datatype to each peer
OFI fit: rank issues FI_ATOMIC_WRITE to each peer
multicast RMA or atomic
1
1
1
5
5
5
9
9
9
bcast
peers may not be in sync when op starts – true for any collective

## Slide 19: All Reduce
MPI_AllReduce(&sendbuf, &recvbuf, count, datatype, op, comm)
Conceptual operation:
  Each rank sends an array of datatype to each peer
  Each rank receives data from each peer
  Each rank applies operation on received data and saves results
Simple OFI fit:
  Each rank sends issues ATOMIC to each peer
  Apply barrier
multicast atomic
1
1
1
5
5
5
9
9
9
sum
3
3
3
15
15
15
27
27
27

## Slide 20: All to All
MPI_AlltoAll(&sendbuf, sendcount, sendtype, &recvbuf, recvcount, recvtype, comm)
Conceptual operation:
  Each rank sends a subarray of datatype to each peer
  Each rank receives a subarray of datatype from each peer
OFI fit: same as conceptual model
‘scatter-cast’
1
2
3
5
6
7
9
10
11
1
5
9
2
6
10
3
7
11

## Slide 21: Reduce-Scatter
scatter
reduce (sum)
MPI_Reduce_Scatter(&sendbuf, &recvbuf, recvcount, datatype, op, comm)
Conceptual operation:
  Each rank sends an array of datatype to lead rank
  Lead rank receives data from each peer
  Lead rank applies operation on received data
  Lead rank sends a subarray of datatype to each peer
OFI fit:
  Each rank sends issues ATOMIC to lead rank
  Lead rank sends a subarray of datatype to each rank
1
1
1
5
5
5
9
9
9
3
15
27
3
15
27
‘scatter-cast’

## Slide 22: All Gather
MPI_Allgather(&sendbuf, sendcount, sendtype, &recvbuf, recvcount, recvtype, comm)
Conceptual operation:
  Each rank sends an array of datatype to each peer
  Each rank receives an array of datatype from each peer
OFI fit: same as conceptual model
multicast
1
5
9
1
1
1
5
5
5
9
9
9

## Slide 23: Requirement Analysis

## Slide 24: Requirement Grab Bag
Need discovery mechanism of available accelerations
Collectives may be repeated millions of times
  E.g. AI training
Collectives may repeat with the same message size
  Computation times may become known
  Communication times may be consistent
Support both pre-defined and user-defined operations
  E.g. MPI collectives and general user functions

## Slide 25: Requirement Grab Bag
Need number of communicating peers
  May involve all or subset of peers in local AV
  Peers likely have matching AV entries
  Data may come from one or all peers
Collectives may be assigned a completion order priority
  May be different than submission order (e.g. AI)
May mix endpoint and fabric accelerators
Ideal to allow plug-in support separate from provider
  Experimental and debug purposes

## Slide 26: network acceleration API requirements
NIC
inline
lookaside
port
NIC
inline
lookaside
port
Discovery mechanism – requires both endpoint and network abilities
Accelerator selection likely managed by network
On-demand functions only
Local and remote peer participation
Long-running functions may save results in network
Input parameters and output results involve multiple endpoints
Accessed through network protocols
May need to program network prior to use

## Slide 27: Observations
General network accelerations
  Need solution similar to SmartNIC proposal
  Lower priority
Collectives
  Some support for both primitive and advanced features
    E.g. RMA, atomics, tagged messages and atomics, triggered ops, collective offload, etc.
  Lots of potential optimizations
    Could lead to wide variety of implementations
    One-size-fit-all solution may be impractical
API enhancements may improve performance without network level offloads
  Repeated messages of fixed size, completion priority

## Slide 28: observations
Collective accelerations are fundamentally different
  All peers must initiate
  Data buffers are identified when collective operation is invoked
Providers must be able to associate transmits and receives as belonging to the same collection operation
  I.e. tagged message buffers are insufficient
  Peers may start the collective operations at different times

## Slide 29: Brainstorming Ideas

## Slide 30: Proposed Vision of Solution
Open source communication framework
Hardware vendor specific implementation
Application driven APIs
Define mechanism to pass input/output parameters and invoke acceleration
Extend existing communication framework to support acceleration functions
APIs targeting application use of specific accelerations

## Slide 31: Current OFI Toolbox
fi_getinfo
  Flexible capability and discovery API
Counters
  Aggregate completions
Triggered operations
  Transfer results after receiving input
Multicast
  Generically defined, but limited by definition to DGRAM EPs
Atomics
  Both RMA and tagged message based

## Slide 32: API Change Process
Identify candidates for API changes
  Ensure there’s a reasonable path forward for most options
Vet list and analyze
Prioritize
Selectively add changes
  Defer where possible
  We may need them all

## Slide 33: Possible Changes
Optional local memory registration
  E.g. FI_MR_LOCAL_OPT
  Allow apps to only sometimes register memory
    Provider must check for valid mr_desc per call
  Optimization for apps that re-use a pool of buffers for collectives, but general buffers for point to point transfers
  Proposal independent from offload support
Multicast atomic operations
  E.g. FI_MULTICAST | FI_ATOMIC
  Enable providers that support a single atomic transfer to multiple destinations
  New flag for atomic query / transfer calls
    Provider can limit which atomic ops are supported

## Slide 34: Possible Changes
Identify multicast target destinations
  Endpoint joins group – fi_join()
    Uses existing API
    Which endpoints belong to group is undefined
    Number of endpoints in group is undefined
  Obtain address representing all addresses in an AV
    New AV call
    Only works if all peer EPs are involved in communication
    May need mechanism to include/exclude entries
  Existing multicast APIs do not match semantics, need something new
Add priority to transfers
  Feasibility of implementation questionable

## Slide 35: Possible Changes
Gathered receive operations
  E.g. FI_MULTI_RECV | FI_TAGGED | FI_RMA
  Merging of multi-receive, tagged messages, and RMA semantics
  Receiver identifies target buffer
  Sender specifies offset
  TBD: determine responsibility for when gather is complete
    User tracks number of receives (e.g. counters)
    Provider performs the tracking (e.g. buffer is fully consumed)
Issue: need to know when entire collective is finished
  I.e. all peers have finished this receive op

## Slide 36: Possible Changes
Network functions for network accelerations
  Proposed for endpoint accelerations
  Network accelerations may require additional semantics
    Asynchronous setup
    More complex input/output

## Slide 37: API Proposal Still as a work in progress

## Slide 38: collective membership
Models
  App fully manages the membership
  OFI manages the membership
App managed membership
  App performs collective to setup membership
  App interfaces to fabric agent to configure resources
  App informs OFI of membership
OFI managed membership
  App informs OFI members
  OFI provider performs collective to setup membership
  Provider interacts with any fabric agents

## Slide 39: collective membership
Two step process
  Identify peer members – local setup (~MPI groups)
  Join collective
    Local setup – app managed membership
    Network setup (~MPI comm creation) – OFI managed membership
Identify members
  New construct – AV Set
  Identifies a subset of addresses in an AV
  Operations to modify and derive new AV Sets
Likely requires AV table
  Provider may not maintain an address list if AV map is used

## Slide 40: AV Sets
fi_av_set(av, attr, fid_av_set **set, uint64_t flags, void *context);
  Defines members for collective operations
fi_av_set_attr
  count – number of members
  start_addr / end_addr – range of address to include as members
  stride – identifies which members in range to include
    Only makes sense for AV table
AV Set operations
  union(set1, set2) set1 = set1 U set2
  intersection(set1, set2) set1 = set1 ∩ set2
  difference(set1, set2) set1 = set1 – set2
  insert / remove

## Slide 41: join group
Treat membership in a collective group the same as a multicast group
fi_join(ep, addr, flags, mc_fid, context)
fi_mc_addr(mc_fid)  fi_addr_t
Join operates asynchronously, writes event to EQ
Assumes all members join collectively
Flags – FI_COLLECTIVE must be set
Addr – references AV Set
Must close group to release any resources
TBD: lifetime of AV Set relative to group
TBD: handle non-universe based joins

## Slide 42: MPI membership Mappings
Some mappings require multiple OFI calls
  OFI has simplified API
fi_av_set()
  MPI_Group_range_incl(Universe, 1, ranges[1][3], *group)
  MPI_Group_range_excl(Universe, 1, ranges[1][3], *group)
fi_av_set_union / intersect / diff
  MPI_Group_union / intersection / difference
fi_av_set_insert / remove
  MPI_Group_incl / excl(group, 1, addr, &group)
fi_join()
  MPI_Comm_create(Universe, group, &comm)

## Slide 43: Collective operations
New FI_COLLECTIVE capability bit
  Secondary capability – provider may offer even if not requested
Access using existing atomic interface
  Uses FI_COLLECTIVE flag to indicate collective operation
    Allows for interpretation of destination address
  Create new static inline wrappers for user convenience
  Details on collectives supported and limits obtained using atomic query APIs
Support most common collective operations
  Limited to those which can map cleanly to the atomic interfaces
  Additional restrictions apply

## Slide 44: barrier
fi_barrier(ep, coll_addr, flags, context)
  flags |= FI_COLLECTIVE
  New datatype FI_VOID
  New op FI_BARRIER
  Destination buffer ignored
fi_atomic(ep, NULL, 0, NULL, coll_addr, 0, 0, FI_VOID, FI_BARRIER, context)

## Slide 45: broadcast
fi_broadcast(ep, buf, count, desc, coll_addr, datatype, flags, context)
  Flags – requires FI_SEND or FI_RECV to identify the source of the broadcast
  buf is treated as either transmit or receive buffer based on flags
  flags |= FI_COLLECTIVE
  op is FI_WRITE
  Destination buffer ignored
fi_atomic(ep, buf, count, desc, coll_addr, 0, 0, datatype, FI_WRITE, context)
  May need to be fi_fetch_atomic() to handle const params
  Could use FI_READ on receive side

## Slide 46: All Reduce
fi_allreduce(ep, buf, count, desc, result, result_desc, coll_addr, datatype, op, flags, context)
  flags |= FI_COLLECTIVE
fi_fetch_atomic(ep, buf, count, desc, result, result_desc, coll_addr, 0, 0, datatype, op, context)

## Slide 47: All To ALL
MPI_AlltoAll(&sendbuf, sendcount, sendtype, &recvbuf, recvcount, recvtype, comm)
Does not map natively to existing OFI calls
  Can map to atomic fetch with restrictions
Can sendtype differ from recvtype in practice?
Can type be replaced with size in bytes?
Will peers use different values for send/recv count?
  I.e. can recvcount be calculated from sendcount and size of collective group?

## Slide 48: All To ALL
fi_alltoall(ep, buf, count, desc, result, result_desc, coll_addr, 0, 0, datatype, context)
  Require same datatype for send and receive buffers
  Results distributed evenly to all peers
fi_fetch_atomic(ep, buf, count, desc, result, result_desc, coll_addr, 0, 0, datatype, FI_ALLTOALL, context)

## Slide 49: Reduce-scatter
fi_reduce_scatter(ep, buf, count, desc, result, result_desc, coll_addr, datatype, op, flags, context)
  flags |= FI_COLLECTIVE | FI_SCATTER
  Need new flag to indicate scattering of results
fi_fetch_atomic(ep, buf, count, desc, result, result_desc, coll_addr, 0, 0, datatype, op, context)

## Slide 50: all-gather
MPI_Allgather(&sendbuf, sendcount, sendtype, &recvbuf, recvcount, recvtype, comm)
Similar issues and discussion as All to All
fi_allgather(ep, buf, count, desc, result, result_desc, coll_addr, 0, 0, datatype, context)
  Require same datatype for send and receive buffers
  Results distributed evenly to all peers
fi_fetch_atomic(ep, buf, count, desc, result, result_desc, coll_addr, 0, 0, datatype, FI_ALLGATHER, context)

## Slide 51: OFI Collective Documentation
Ordering
  Completion ordering definition unchanged
  Collectives of the same type matched with peers based on submission order
    Same atomic call, operation, and data type
Completions
  Operations are asynchronous (same as other transfer operations)
  Notification via CQ or counter increment
Support
  Indicated by FI_COLLECTIVE capability bit
  Details via atomic query calls

## Slide 52: THANK YOU