## Slide 1: Traffic Classification
Paul Grun, Jim Swaro
April 2019
Cray, Inc

## Slide 2: Two parts
Objective: Presently, libfabric doesn’t provide a mechanism for a consumer to express to the provider any information related to traffic classification or QoS
Part One (this slide deck) – discusses ideas for how to label traffic classes and what those labels mean
Part Two (coming later) – how to communicate traffic classification information across the libfabric API

## Slide 3
Consumer
Provider
Driver
H/W
API
How are those labels exposed across the API?
How are those labels interpreted by the fabric interface??
Hints and capabilities.
How does consumer know what options are available?
What labels are available to the consumer to request certain QoS?
A conundrum
- Want to allow a consumer to provide guidance on its reqmts, but
- Also want to allow for varying fabric implementations

## Slide 4: What’s the correct abstraction?
HPC and classic IP apps may have different preferred levels of abstraction
  As well as different basic objectives
We want an abstraction that is low enough to give the consumer sufficient control over traffic classification,
But not so low as to dictate specific Per Hop Behaviors (PHB)
  PHB determines the characteristics of a data flow as it traverses a network.
Per Hop Behaviors are not standardized and are a function of the characteristics of the underlying fabric

## Slide 5: HPC, IP
HPC and classic IP apps may require different preferred levels of abstraction in Traffic Classification
  HPC traffic may be well-served by a fairly abstract classification of traffic into a small number of classes
  IP applications are well-served by the well-defined Diffserv Architecture
IP service differentiation has a broad mandate to provide highly granular traffic control across a wide range of services, provisioning policies, and environments
HPC traffic is generally classified much more narrowly
There is some overlap between HPC and IP, but IP-based service differentiation is much richer due to its broad mandate
We propose that the libfabric API should support:
  The Diffserv architecture in order to fully support IP traffic
  A Diffserv-like architecture focused on HPC

## Slide 6: diffserv
Diffserv is a well-defined scheme for implementing scalable service differentiation across the internet
Diffserv architecture is characterized by:
  Traffic entering a network is classified and conditioned at the network boundary.
  Classification results in the assignment of a ‘code point’ (DSCP) to a data flow
  A code point maps to a set of Per Hop Behaviors (PHBs) defining the observable forwarding behavior applied to a data flow
Essentially, Diffserv architecture differentiates between:
  The conditioning and classifying functions that are implemented only at the network edge, and
  The Per Hop Behaviors implemented in the interior of the network, with the same set of behaviors begin applied to all data flows carrying the same classification

## Slide 7: DSCP
DiffServ defines the Differentiated Services Code Point - DSCP
  A label carried in the header describing how a data flow to which a specific set of Per Hop Behaviors can be applied
A six bit field carried in the header allowing up to 64 separate classifications
Not all 64 are commonly used - there are 21 “well-known” DSCP aliases
  Established only by convention, not by specification

## Slide 8: HPC
HPC requirements are more straightforward
  Predictable run times
  Relative application priorities
  Dedicated application bandwidth
  Management of latency sensitive flows
  Management of I/O intensive applications
  Control of packet loss during micro-burst congestion

## Slide 9: Proposal: Best Practices Traffic Classes
Low latency - This class supports low latency, low jitter data patterns typically caused by transactional data exchanges, barrier synchronizations, and collective operations that are typical of HPC applications. Specified maximum latencies are requested by this class. Fulfillment of such requests in this class will typically require accompanying bandwidth caps and packet size limitations so as not to consume excessive bandwidth at high priority.
Dedicated Access - This class provides a category that will operate at the highest priority. It carries a high bandwidth allocation, maximum latency targets, and the highest scheduling and arbitration priority. This class has absolute priority over all others.
Bulk Data - This class is intended primarily for large data transfers associated with I/O and is present to separate sustained data transfer from other application inter-process communications.
Best Effort - This is the default, shared class, carrying the traffic for a number of applications executing concurrently over the same network infrastructure. Even though it is shared, network capacity and resource allocation are distributed fairly across the applications.
Scavenger Class - This class is used for data that is desired but does not have strict delivery requirements. A good example of this is monitoring data, especially for application specific monitoring such as with performance tools. Global monitoring could also be done this way for data that is too voluminous for out-of-band transport. Using this class makes sure that such communication does not interfere with communication doing “real” work.

## Slide 10: Feedback received on initial proposal
Request from MPI user:
  Dedicate the existing Bulk Data class specifically for I/O – Bulk I/O Data
  Add an additional Bulk Data class dedicated to large message operations, e.g. rendezvous operations – Bulk IPC Data
Feedback from OFIWG
  Add a high priority class for fabric management, PTP, etc. – Mgmt Class
  Alternatively, plan to use the existing low latency class for high priority management traffic
Synchronous vs Asynchronous operations?
  Strawman – setting Traffic Class is an asynchronous operation – discussion?
Feedback from OFIWG - Consider adding a class/label specifically for checkpoint
  Options are to use the existing Bulk Data class or Dedicated Access class
  Some felt that there might be value in a dedicated label, even if it aliases directly to another existing label
  Given the above, there does not seem to be a need for a class dedicated to checkpoint. It can be handled as:
    Bulk I/O Data
    Bulk IPC Data
    Dedicated Access

## Slide 11: Updated Proposal: Best Practices Traffic Classes
Low latency - This class supports low latency, low jitter data patterns typically caused by transactional data exchanges, barrier synchronizations, and collective operations that are typical of HPC applications. Specified maximum latencies are requested by this class. Fulfillment of such requests in this class will typically require accompanying bandwidth caps and packet size limitations so as not to consume excessive bandwidth at high priority.
Dedicated Access - This class provides a category that will operate at the highest priority, except the Mgmt Class. It carries a high bandwidth allocation, maximum latency targets, and the highest scheduling and arbitration priority.
Bulk IPC Data – This class is intended to support large IPC transfers such as MPI rendezvous operations.
Bulk I/O Data - This class is intended for large data transfers associated with I/O and is present to separate sustained I/O transfers from other application inter-process communications.
Best Effort - This is the default, shared class, carrying the traffic for a number of applications executing concurrently over the same network infrastructure. Even though it is shared, network capacity and resource allocation are distributed fairly across the applications.
Scavenger Class - This class is used for data that is desired but does not have strict delivery requirements such as monitoring data especially for application specific monitoring such as with performance tools. Global monitoring could also be done this way for data that is too voluminous for out-of-band transport. Using this class makes sure that such communication does not interfere with communication doing “real” work.
Mgmt Class – This class is intended for traffic directly related to fabric (network) management. It should not be used by standard user or kernel applications.

## Slide 12: Proposal: labels + DSCP values
Develop a scheme that:
Includes the usual hints mechanisms to allow a consumer to request specific services and the provider to respond with its capabilities
Allows HPC-specific labels to be transmitted across the API, or
Allows specific DSCP values to be transmitted across the API (but not both) to meet the meets of classical IP-based applications

## Slide 13
Consumer
Provider
Driver
H/W
API
How are those labels interpreted by the fabric interface??
What labels are available to the consumer to request certain QoS?
Proposal
Either a) a six bit DSCP value, or one of five defined HPC labels

## Slide 14: Results of 4/23/19 meeting

## Slide 15: Discussion
Consider adding a class/label dedicated to fabric management.
Consider adding a class/label specifically for checkpoint
  Options are to use the existing Bulk Data class or Dedicated Access class
  Some felt that there might be value in a dedicated label, even if it aliases directly to another existing label
The scheme being proposed assumes that changing traffic classes is relatively heavy weight, thus applications are discouraged from changing traffic classes
  The implication is that an application that wishes to change traffic classes for some reason would incur a resource penalty for doing so.
  The alternative is a more complex mechanism allowing fast changes in traffic classification at a significant increase in complexity.
  It seems likely that traffic in different classes will likely be targeted at different endpoints anyway
  The sense of the body is that the proposal makes the right tradeoff
Is there a way to enforce conformance, and/or to balance traffic between jobs?
  Enforcement would be a function of the policing and/or drop features at fabric ingress, which is to say a function of the provider and below the level of the libfabric API.
  Balancing traffic between jobs is believed to be a function of a work load manager or some other management function and is above the level of the libfabric API
  One member suggested that this may be an area that the OFA may want to explore in the future, out of the context of OFI.
Should setting of traffic classes be a synchronous or asynchronous operation?
  If, for example, executing an FI_SET_OPT requires a transit across the fabric, an asynchronous call may be preferred.

## Slide 16: Bonepile (don’t read beyond here yet)

## Slide 17: DSCP
A six bit field carried in the header allowing up to 64 separate classifications
Not all 64 are commonly used - there are 21 “well-known” DSCP aliases
  Established only by convention, not by specification
DSCP value | PHB
XXX000 | Class Selector (Precedence / Priority)
000XX0 | Best Effort (Default)
001XX0 | Assured Forwarding
010XX0 | 
011XX0 | 
100XX0 | 
101110 | Expedited Forwarding
From this come 5 DiffServ service classes:
  Best Effort
  Assured Forwarding
  Expedited Forwarding
  Conversational services
  Network control

## Slide 18: Five well-understood DSCP classes
Best Effort – Like the man says. The router does not apply any special QoS handling to packets with 000000 in the DiffServ field, a backward compatibility feature. There is usually a high probability that these packets will be dropped under congested network conditions.
Assured Forwarding – The router offers a high level of assurance that the packets are delivered as long as the packet flow from the customer stays within a certain service profile (the service provider defines the values). The router accepts excess traffic but applies a random early discard (RED) drop profile to decide if the excess packets should be dropped and not forwarded. Three drop probabilities (low, medium, and high) are defined for this service class.
Expedited Forwarding – The router delivers assured bandwidth, low loss, low delay, and low delay variation (jitter) end-to-end for packets in this service class. Routers accept excess traffic in this class, but in contrast to assured forwarding, out-of-profile expedited-forwarding packets can be forwarded out of sequence or dropped.
Conversational Services – The router delivers assured (usually low) bandwidth with low delay and jitter for packets in this service class. Packets can be dropped, but are never delivered out of sequence. Packetized voice is a good example of a conversational service.
Network Control – The router delivers packets in this service class with a low priority (these packets are not delay-sensitive). Typically, these packets represent routing protocol hello or keepalive messages and loss of these packets jeopardizes proper network operation, so delay is preferable to discard.