## Slide 1: OFI Support for Heterogeneous memory
Sean Hefty, OFIWG Co-Chair
March 2019
Intel Corporation

## Slide 2: Overview
Support data transfers to/from/between peer devices
  GPUs, FPGAs, persistent memory
    Examples only, solution is mostly independent from type of device
  PCI peer to peer transfers
    E.g. GPU to RDMA NIC, GPU to GPU
    Implementation agnostic, e.g. could use bounce buffers
Application examples:
  Machine learning, deep learning, AI, MPI
Scope is limited to fabric communication (i.e. we’re not trying to be the interface for the accelerator itself)

## Slide 3: Related
Support libfabric running on non-host cores
Invoke accelerator functionality as part of transfer
  Covered by separate SmartNIC proposal
File system backed memory regions
  Transfers to/from storage without mapping file into process VA space

## Slide 4: Definitions
Heterogeneous memory (HMEM)
  Non-host memory (e.g. PCI device memory)
Unified address space
  Memory may be mapped into virtual address space of process
    Without unified virtual address space, RMA may require FI_MR_RAW
Peer software interface
  Software interface to access peer device / allocate memory
  E.g. CUDA, OpenCL
  Compile and/or run time option?
  May need to support multiple SW interfaces simultaneously from single app
Proposal only – work in progress

## Slide 5: Requirements
SW may directly access HMEM device
  E.g. execute GPU kernels
  Most efficient if SW marks addresses as HMEM or not
    Need to include device identifier
Middleware may lose HMEM association
  Rediscover HMEM properties
  Pass properties between app and OFI external from middleware
    e.g. per-thread global variables
Memory may be allocated using specialize functions
  e.g. cudaMalloc vs malloc

## Slide 6: Requirements
Unified address space is optional
Virtual to physical may change dynamically
  CPU to GPU, or between GPUs
  Assumes unified address space
  Network may need to locate the physical region at time transfer occurs
  Transfer may be initiated by a peer (e.g. RMA read/write)

## Slide 7: Proposal
Support two models:
HMem hooking provider
  Support existing HMEM (e.g. CUDA) aware applications
  Enables peer to peer transfers for any provider
  Introduces checks into fast path operations
    But only when hook is enabled
  Providers can leverage implementation
  Limited initial implementation, expand as needed
    First version will target CUDA
Direct API support
  Allow application to specify when heterogeneous memory is used
  Can optimize performance path
  Drives changes through the providers

## Slide 8: HMem Hooking Provider
HMem Hook
Ex: MPI with GPUDirect Support
Peer Interface
Ex: CUDA
Provider(s)
Ex: RxM + Verbs
OFI (HMEM not specified)
OFI w/ HMEM Support
OFI Core
HM Infrastructure
Ex: MR Cache
Host or device address?
May optimize host vs HMem transfers differently
Drive API changes down
Setup HM transfers
Mythical Kernel Driver Services (HMM, MMU Notifier, etc.)
Request transfer
Register HMem

## Slide 9: HMEM Hook
Hooks enabled through environment variables
Hook infrastructure was restructured to look more like other providers
  Update core to allow app to specify hooks programmatically when opening a fabric
  Add list of desired hooks to end of provider name(s) when opening fabric

## Slide 10: OFI Extensions
Capability bit: FI_HMEM
  Requests/indicates support for transfers to/from heterogeneous memory
  Implementation agnostic
    May use PCI peer to peer transfers or host bounce buffers or …
  Secondary capability bit – provider may set even if app doesn’t request
mr_mode bit: FI_MR_HMEM
  Require memory registration for heterogeneous memory
    For P2P setup, even if registration isn’t needed by NIC
  FI_MR_LOCAL refers to host memory

## Slide 11: OFI Extensions
MR: peer SW interface
  Need to specify peer SW library
  Version?
MR: device identifier
  Can require that device context is set or discoverable by provider based on input
MR: device memory address
  Pass in as addr
  Requires mapping into VA space
CUDA
  Device id is index
  May be set globally prior to calls
  cudaSetDevice(int device)
  cudaGetDevice()
  cudaMalloc(**ptr, size)
OpenCL
  cl_context = array of devices
  clSVMAlloc(dev_type .. dev_id ..)
Short-term: FI_P2P_API env var
Extend mr_attr or add new mr_ops later if needed