## Slide 1: Universal Fabric Management For Tomorrow’s Data Centers

## Slide 2: The Ecosystem for Fabrics in Datacenters is Changing
Fabric Landscape is Changing
Rapidly increasing types of fabric interconnects
Each fabric has its strengths, features, and management tools
Each fabric has its own configuration mechanisms and interfaces
Workload and Resource Ecosystem is changing
New compute and storage resources are becoming available
HPC Clusters and Cloud Computing environments
  running increasingly diverse and dynamic workloads
  incorporating both distributed computing capabilities and heterogeneous hardware

## Slide 3: This Creates Problems in Manageability
Administrative Management Challenges
No common fabric manager interface or fabric model available to link applications with remote resources
Workload management and optimization is different for each type of fabric
Administrators are being asked to manage an increasing heterogenous fabrics infrastructure, each with its own management standard and model`
Fabric Services
Slurm
User APPs & Libraries
Gen-Z
Fabric Manager
Gen-Z
HW
Fabric Services
IB
Ethernet
…
Ethernet
Fabric Managers
Eth
HW
IB
Fabric Manager
…
Fabric Manager
IB
HW
…
HW
Fabric Services
AWS
PBS
Kubernetes
Orchestration Managers
Proprietary
Fabric Manager
AWS
HW
…
…
…
Ethernet
TBD
Fabric Managers
TBD
HW
Fabric Services
Gen-Z
Fabric Services
Fabric Services

## Slide 4: We Can Fix These Management Problems
Need interoperability through common interfaces to enable managers to efficiently connect workloads with resources
Need to Integrate an Open Fabrics Management Framework (OFMF) with standards-based Ecosystem management
Without an Open Fabric Management Framework:
    Every tool and every middleware library provider needs a unique call to a specific fabric management stack for each available fabric
With an Open Fabric Management Framework:
    Everyone calls common fabric services to manipulate the Redfish fabric model
    Open Fabrics Management Framework triggers fabric specific providers to make the actual changes in the fabric
Slurm
User APPs & Libraries
Gen-Z
Fabric Manager
Gen-Z
HW
Fabric Services
IB
Ethernet
…
Gen-Z
Ethernet
Fabric Managers
Eth
HW
IB
Fabric Manager
…
Fabric Manager
IB
HW
…
HW
Fabric Services
Fabric Services
AWS
PBS
Kubernetes
Orchestration Managers
Proprietary
Fabric Manager
AWS
HW
TBD
Open Fabric Management Interface
Fabric Services
Fabric Services

## Slide 5: Examples of Fabric Admin Services Offered by OFMF
The Open Fabrics Management Framework
Control Services
  Discovery
  Inventory
Communication Services
  Connection Management
  Address vectors
Partition Services
  Zones
  Connections
Messaging Services
  Queues and Contexts
  Events and Errors
  Atomics and other synchronizations
Security
  Sub-fabrics which provide exclusionary access security
Slurm
User APPs & Libraries
Gen-Z
Fabric Manager
Gen-Z
HW
Fabric Services
IB
Ethernet
…
Gen-Z
Ethernet
Fabric Managers
Eth
HW
IB
Fabric Manager
…
Fabric Manager
IB
HW
…
HW
Fabric Services
Fabric Services
AWS
PBS
Kubernetes
Orchestration Managers
Proprietary
Fabric Manager
AWS
HW
TBD
Open Fabric Management Interface
Fabric Services
Fabric Services

## Slide 6: Open Fabric Management Framework Architecture
Administration Domain
abstract manipulations
SLURM
Kubernetes
Providers
Framework
OFMF Domain
Hardware
Partition Mgmt
Events & Logs
Authentication
Peer Address Lookup
Gen-Z
Slingshot
IB
Create Zone
Create Partition
Redfish
/
Swordfish
Model
Native
Model
Create Partition
libfabric
openFAM
Application Domain
Create zone
FAM Resource
Manager
Clients
attach shared memory region
create shared memory region
Resource Inventory
OFMF Services
Actual Fabric
Notes: This slide builds the block diagram architecture of the OFMF:
1)Left side is the user/admin/orchestration/automation domain(s)
2)Right side is the hardware that makes up the fabric and the resources that are accessed thereon
3)The middle is a representation of the functional blocks making up the OpenFabrics Management Framework
4)On the left, various workload managers, app/ libraries, and resource managers are represented. They are all clients of the Framework
5)Inside the OFMF the state of all the fabrics being represented to the clients are represented using a Redfish fabric model
6) At the right border of the OFMF there are fabric specific providers for each of the fabrics which the OFMF is supplying common services for, and each provider may have its own native model of its specific fabric
7)Any entity (SW tool, admin GUI, shell script via CLI) may need to create a virtual platform, pod, cluster, partition, vLan, job queue, subnet or other name for a set of resources that are connected together to enable some workload(s) to execute while being isolated from other jobs.
Such an entity needs a common taxonomy for describing the resources needed in the set and how the connections among them are to behave.
We are proposing to use the DMTF’s Redfish standards to model the fabric and its resources, and to provide the RESTful interfaces through which the entities on the left can learn of the modelled resources and create such a set of fabric resources.
8)Redfish currently has an object called a ‘zone’ that contains a list of the fabric endpoints which may be connected to each other. Zones can be used to enumerate the members of a vLAN, or the resources of a virtual platform.
9)The framework will update the Redfish model for the given fabric(s) and exchange the appropriate details with the fabric specific provider(s)
The Providers are responsible for updating any native models they maintain of their fabric and to issue the appropriate traffic to the fabric hardware
10) It is important to note that ‘admin tools’ are not the only clients of the OFMF services.
Applications and Resource Managers will need runtime support in the form of creating, registering, attaching, and freeing shared memory regions
OS and virtual machine managers will need an interface to request initial (boot time) resource allocations and runtime changes, as well as authentication and events and logging services.

## Slide 7: Integrating Open Fabrics Management Framework into a Standards-based Enterprise and Datacenter Management Ecosystem

## Slide 8: What are Redfish and Swordfish?
DMTF Redfish™ covers server, data center, fabric management
  REST API with JSON payloads; choice of CSDL, JSON and YAML schema for development
SNIA Swordfish™: Storage Management Specification with REST Based API
  Extends DMTF’s Redfish Specification
Swordfish adds storage management to all of these use cases, plus storage fabric management:
  Covers block, file, and object storage
  Extend traditional storage domain coverage to include converged environments (servers, storage and fabric together)
  Provides the option for implementation to utilize Class of Service (intent or service level) based provisioning, management, and monitoring
  Through Alliance partnerships with NVM Express®, RF/SF (Redfish and Swordfish) have added NVMe / NVMe oF manageability

## Slide 9: Redfish Hierarchy
Subordinate
Resource
Collections
./TaskService
/redfish/v1
“Logical View”
Collection
Resource
Singleton
Resource
Volumes
Service Root
Singleton
Resource
./Systems
Systems/<id>
Processors
Processors/<id>
“Management”
./Managers
“Physical View”
./Chassis
Chassis/<id>
./EventService
./AccountService
./SessionService
Redfish services for account management, events, logs, tasks, session / certificates, etc.
…
Drives contained in chassis, managed in storage.
Volumes
Storage
Storage/<id>
Volumes
EthernetInterface
EthernetInterface/<id>
Volumes
Drives
Drives/<id>
Volumes
Power
Power/<id>
Volumes
Thermal
Thermal/<id>
Managers/<id>
Volumes
LogService
LogServices/<id>
Volumes
NetworkProtocol

## Slide 10: Redfish Hierarchy: Adding Swordfish Advanced Storage
/redfish/v1
Storage Collection
Collection
Resource
Singleton
Resource
Volumes
Subordinate
Resource
Collections
Service Root
Singleton
Resource
Reference (link) to Volume
./Storage
Storage/<id>
Volumes
Volumes/<id>
StoragePool Collection
./StoragePools
StoragePools/<id>
SwordfishNVMeDrive, v1.0.0
/redfish/v1/Registries/AdvertisedFeatures
Features Registry contains the published supported Features.
Swordfish schema (Controllers, Volumes, StoragePools, etc) attach to storage.
./Registries
Chassis Collection
./Chassis
Chassis/<id>
Volumes
Drive Instance
Drives
Drives/<id>
StoragePool Collection
Volume (Namespace) Instance
./AllocatedVolumes
AllocatedVolumes/<id>
./EventService
./AccountService
./SessionService
NVMe Device Usage:
Subsystem == Storage
Controller == StorageController
Volume == Namespace
StoragePool == Endurance Group / NVM Set
Chassis / Drive == Physical Entity Information
StorageControllers Collection
./Controllers
Controllers/<id>
Redfish services for account management, events, logs, tasks, session / certificates, etc.
…
Drives contained in chassis, managed in storage pools.

## Slide 11: Redfish/Swordfish Hierarchy: Adding Fabrics
/redfish/v1
Collection
Collection
Resource
Singleton
Resource
Volumes
Subordinate
Resource
Collections
Service Root
Singleton
Resource
Reference (link) to Volume
./Storage
Storage/<id>
Volumes
Volumes/<id>
Collection
./StoragePools
StoragePools/<id>
Collection
Volume (Namespace) Instance
./AllocatedVolumes
AllocatedVolumes/<id>
NVMe oF:
Adds Fabric and access rights
StorageControllers Collection
./Controllers
Controllers/<id>
Collection
./Fabrics
Fabrics/<id>
Collection
./Connections
Connections/<id>
Collection
./Zones
Zones/<id>
Collection
./Endpoints
Endpoints/<id>

## Slide 12: Redfish/Swordfish Hierarchy: Extending Fabric Management
/redfish/v1
Collection
Collection
Resource
Singleton
Resource
Volumes
Service Root
Singleton
Resource
Reference (link) to Volume
./Storage
Storage/<id>
Volumes
Volumes/<id>
Collection
./StoragePools
StoragePools/<id>
Collection
Volume (Namespace) Instance
./AllocatedVolumes
AllocatedVolumes/<id>
NVMe oF:
Adds Fabric and access rights
StorageControllers Collection
./Controllers
Controllers/<id>
Collection
./Fabrics
Fabrics/<id>
Collection
./Switches
Connections/<id>
Collection
./Zones
Zones/<id>
Collection
./Endpoints
Endpoints/<id>
OpenFabrics Management Framework

## Slide 13: Managing Tomorrow’s Fabrics
Orchestration Tools
Composing Tools / Resource Managers
Fabric Management Stack
Route & Topology Management
Addressing / Firewalling / Partitioning
Low-level Fabric setup / Authentication & Routes
Fabric Services
IB
RoCE
Ethernet
Compute
Storage
Memory
Fabric
Configuration Requirements
Endpoint
Configuration Requirements
Ecosystem Management
Open Fabric Management Framework

## Slide 14: Expanding Standardized Fabric Management Through Alliances

## Slide 15: SNIA and OFA Working Together
Through Alliance Agreements
Bring the technical teams from the organizations together to align existing work
  SNIA brings storage and storage fabric management and domain expertise
  OFA helps accelerate the development and adoption of advanced fabrics for the benefit of advanced fabrics ecosystems
Create new content in each area as needed
Fabric Management
Open Fabric Management
Storage Fabric Management

## Slide 16: Planned Work Items
Gather more client-driven use-cases
  Use OFA identified Use Case Descriptions and Flow Diagrams to confirm property / object completeness
Map together RF/SF management interface with OFA Open Fabric Manager functionality
  Redfish and Swordfish provide the OFA Fabric Manager with NVMe-oF instantiation for current fabric conditions
  Step through use-cases to validate RF/SF extensions
Ensure wide fabric management coverage e.g.,
    Gen Z
    Slingshot
    InfiniBand
    OmniPath
    RoCE
    iWarp
    Ethernet
    FC
    Future unknown fabrics
Client
End user of solutions package
Applications Developer
Creates application, ties into hardware
Solutions Provider
Integrating application with infrastructure
OFMF
Interoperability

## Slide 17: Thank you for watching Join the OFMF Working Group to learn more and to contribute
SNIA Swordfish™
Swordfish Standards
  Schemas, Specs, Mockups, User and Practical Guide`s, … https://www.snia.org/swordfish
Swordfish Specification Forum
  Ask and answer questions about Swordfish
  http://swordfishforum.com/
Scalable Storage Management (SSM) TWG
  Technical Work Group that defines Swordfish
  Influence the next generation of the Swordfish standard
  Join SNIA & participate: https://www.snia.org/member_com/join-SNIA
Join the SNIA Storage Management Initiative
  Unifies the storage industry to develop and standardize interoperable storage management technologies
  https://www.snia.org/forums/smi/about/join
Open Fabric Management Framework
OFMF Working Group (OFMFWG)
  Description & Links
  https://www.openfabrics.org/working-groups/
OFMFWG mailing list subscription
  https://lists.openfabrics.org/mailman/listinfo/ofmfwg
Join the Open Fabrics Alliance
  https://www.openfabrics.org/membership-how-to-join/
DMTF Redfish™
Redfish Standards
  Specifications, whitepapers, guides,… https://www.dmtf.org/standards/redfish