## Slide 1: Open Fabrics Management Framework Development
SC21 OFMF/Gen-Z PoC
Notes: The following slides are not intended to be a tutorial on the OFMF, the Redfish fabric model, or use case analysis. Many, many details are lacking, and we aren’t going to attempt to fill in all the details in this BoF session.
The following slides are simply a very quick overview of the goals of the OFMF project and its basic architectural assumptions, the working strategy of the OFMF work group, and how Redfish is a major cog of the final solution.

## Slide 2: Agent Contents
1. Tentative schedule dates and steps
2. Use-Case Description
Boundaries
Top-Down Approach using decompositions and pipe-and-filter approach
UML

## Slide 3: Tentative schedule dates and steps
Requirements Analysis----Now!
System Design----
Program Design-–
Program Implementation----
Testing and Training on Software----Early September
Initial POC at SDC21-----Middle of September
Final Testing---2nd Week of October
Training on Demo
SC21----week before Thanksgiving

## Slide 4: Use-Case Descriptions
Use Case Description | Fabric Resource Hot Subtract
Actors | OFMF Fabric Manager, Administrator, Fabric Subnet Manager
Description | Add components when detected by a Subnet Manager
Normal Flow | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric The Subnet Manager finds a missing endpoint The Subnet Manager deletes the endpoint The Subnet Manager communicates to the Agent that a deletion has been made to the fabric The Agent notifies OFMF that a fabric change has occurred The OFMF does a Get to request the Agent to identify the change The OFMF updates the Redfish tree with the deletion through a post of new information Success is reported
Alternate Flow 1 | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric No deletion is identified
Alternate Flow 1 | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric The Subnet Manager finds a missing endpoint The Subnet Manager deletes the endpoint The Subnet Manager communicates to the Agent that a deletion has been made to the fabric The Agent fails to update the Redfish tree to remove the endpoint Failure is reported

## Slide 5: Use-Case Descriptions
Use Case Description | Fabric Resource Hot Subtract
Actors | OFMF Fabric Manager, Administrator, Fabric Subnet Manager
Description | Subtract components when is detected by a Subnet Manager
Normal Flow | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric The Subnet Manager finds a missing endpoint The Subnet Manager deletes the endpoint The Subnet Manager communicates to the Agent that a deletion has been made to the fabric The Agent notifies OFMF that a fabric change has occurred The OFMF does a Get to request the Agent to identify the change The OFMF updates the Redfish tree with the deletion through a post of new information or delete OFMF reports to clients that a modification to the fabric has occurred.
Alternate Flow 1 | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric No deletion is identified

## Slide 6: Boundaries
Responsibility of the Agent
  Notify OFMF of changes of fabric endpoints, switches and FAM
    Event interface
  Support standard Redfish
    Post, Patch, and Delete only for POC
  The Agent needs to use Simple Service Discovery Protocol (SSDP)
    We will determine for the POC the amount of time/work available
Security Concerns
  How much of the Redfish Aggregation model do we follow?
    We need to decide whether to support Session+ authentication
  Clients cannot interact in its roll with the Agents
Limits of the Agent
  Will interact with the Subnet Manager
  Will interact with the OFMF
    Changes will be made directly to Redfish
  OFMF Clients cannot interact with the Agents directly
  Agents cannot control the fabric infrastructure -–Subnet Manager responsibility

## Slide 7: Subnet Manager start-up
Scan Fabric
Forward and equivalent event in Redfish
change
Yes
No
Update OFMF Redfish
Maintain current state
Lookup change in table

## Slide 8: Top-Down Approach

## Slide 9: Subnet manager scan and modify OFMF redfish
OFMF
Agent 2
Agent 3
Agent n
Agent 1
Subnet Manager
Subnet Manager can talk to 1 or more Agents

## Slide 10: Subnet manager scan and modify OFMF redfish
OFMF
Agent 2
Agent 3
Agent n
Agent 1
Subnet Manager
Agent communicates to the OFMF using Redfish

## Slide 11: Agent Top-Down design
Agent
OFMF Redfish Communicator
Event translator
(Look-up Table?)
Forward an equivalent event in Redfish
Subnet Manager Event Receiver
Create a task list
Maintain Current State/Intended State/Health State

## Slide 12: Pipe and Filter