## Slide 1: NetworkX JSON output decoding
Key:Value pairs of NetworkX flags
Key:Value pairs of NetworkX details within the graph
  Fabric UUID : value created by FM
  Array of MGR_UUIDs per Gen-Z [
    128-bit UUID created by FM(s) per Gen-Z
    Array in case there are more than one FM
  PFM: C-UUID:SN of primary FM
Array of nodes:
Nodes also consist of Key:Value pairs
  instance UUID: unique node UUID (assigned by FM)
  cclass: component_class value per Gen-Z control structure
  manager UUID: MGR_UUID assigned by primary manager
  gcids: Array of global CIDs (HEX digits as TEXT)
  SID:CID #an array because up to 4 GCIDs/component
  fru_uuid: value per Gen-Z control structure
  max_data: memory storage capacity in bytes
  max_iface: max number of Gen-Z interfaces on node
  cstate: C-UP|C-CFG component state per Gen-Z
  id: globally unique Gen-Z ID (based on concatenating)
  C-UUID : component SN
  # C-UUID and SN are from Gen-Z control structure
JSON list of key:value pairs

## Slide 2: NetworkX JSON output decoding
Array of links between nodes
Each link
Each endpoint of a link has a dictionary of Key:Value pairs bound to the instance_uuid of the node:
  num: GCID. port number for this end of the link
  State: I-Up | I-Dn et. al. from Gen-Z spec for interface state
Key:Value pairs identifying the Gen-Z resources at both ends of the link by their globally unique ID crafted from C-UUID and device SN
“source”: id using C-UUID:Serial Number
“target” : id using C-UUID:Serial Number
NetworkX defines source and target labels, but they mean nothing to Gen-Z and Redfish
Key:Value pair defined by NetworkX and by NetworkX to track number of extra links between same endpoints. No significance to Gen-Z and Redfish, though values >0 may imply redundant links are present.
State of the PHY associated with this interface is contained in another sub-dictionary containing
PHY Status, and Link Width Reduction flags
Other endpoint description

## Slide 3: Zephyr Config File Decoding
fabric_uuid of fabric being described
Array of ‘resources and a relationship between them’
Class_uuid: SW/ FM assigns this based on how resource is to be used, IE, if memory module & is block_mode, it has this ‘class_uuid’.
Instance_uuid: UUID assigned (by RM?) of this memory chunk
Flags: values specific to class type (driver type)
Class: cClass value from Gen-Z spec, ‘17’ = block mode memory
Memory: [array of memory attributes as key:value pairs] # associated within a specific ‘resource’
  Length: in bytes
  Type: 0 = control space, 1 = data space, 2 = interleaved data space
  ro_rkey: 32 bit read-only RKEY value for this memory chunk
  rw_rkey: 32 bit read-write RKEY value for memory chunk
{
"fabric_uuid": "4e26e323-23c2-4480-a7e1-1e820dd499c5",
"add_resources": [
{
"producer": "859be62c-b435-49fe-bf18-c2ac4a50f9c4:0x0000000000012345",
"consumers": ["e3331770-6648-4def-8100-404d844298d3:0x00000000000abcde"],
"resources": [
{
"class_uuid": "3cb8d3bd-51ba-4586-835f-3548789dd906",
"instance_uuid": "???“
"flags": "0",
"class": 17,
"memory": [
{
"start": 0,
"length": 21474836480,
"type": 1,
"ro_rkey": 0,
"rw_rkey": 0
} ] } ] } ] }
Producer: id # FM assigned id using vendor C-UUID:SN
Consumers: [array of id values of consumers]
Resources: [array of Key:Value pairs] that describe the ‘producer’ resources
Add_resources: really an action that creates a ‘connection’ between the producer node (a memory module in this case) and one or more consumer nodes (servers?).

## Slide 4
Clients locate the OFMF services via SSDP M-search
Clients may use any representation of fabric resources internally, but speak Redfish to OFMF
OFMF Services listens for clients and responds to M-search requests
OFMF locates Agents by responding to SSDP M-search requests issued by Agents
Agents issues M-search looking for OFMF – (or issues NOTIFY??)
Agent polls (what protocol?) every 5 seconds for Zephyr
Zephyr receives Flask endpoint from Agent ??
Zephyr responds to Agent requests sent via HTTP
Fabric Hardware
Fabric specific
SW
config
Redfish
model
FM
GUI / CLI
FAM Manager
Composition Manager
OFMF
Services
Fabric Manager
agent
admin
Redfish
Redfish
FM API
Storage
Manager
Image Manager
Apps
Systems
1
Endpoints
1
Switches
SW1
Fabric Adapters
1
Ports
1
2
Ports
1
2
6
3
3
Ports
1
2
3
4
5
6
3
8
9
a
b
ServiceRoot
<FabricType>
Structure of the OpenFabrics Management Framework

## Slide 5
Clients use HTTP CRUD protocols to converse with OFMF Services and manipulate Redfish fabric objects
OFMF sends relevant Redfish requests to fabric Agent, also via HTTP
Agent and Zephyr FM exchange messages via proprietary (application/JSON) RESTful interface
  HTTP transport
  JSON data payload but ...
  not a Redfish data schema
  Not a Redfish URI
Gen-Z Fabric Hardware
Fabric specific
SW
config
Redfish
model
FM
GUI / CLI
FAM Manager
Composition Manager
OFMF
Services
Linux
Gen-Z FM
agent
admin
Redfish
Redfish
FM API
Storage
Manager
Image Manager
Apps
Systems
1
Endpoints
1
Switches
SW1
Fabric Adapters
1
Ports
1
2
Ports
1
2
6
3
3
Ports
1
2
3
4
5
6
3
8
9
a
b
ServiceRoot
<FabricType>
Structure of the OpenFabrics Management Framework