## Slide 1: Working towards adoption with…
OpenFabrics
Management
Framework
Today

## Slide 2
Companies & entities involved in the OFMF Project

## Slide 3: Why create a new Fabric Manager Framework?
New HPC and Cloud computing designs are becoming more heterogeneous to be able to handle more and different types of computing tasks
  More available types of HPC applications and tools
  Machine Learning
  Deep Learning
New alternative network fabrics, new ways to deploy memory, and custom accelerators are being dreamed up to maximize performance for specialized tasks.
Notes: Current intractability of handing Enterprise work versus HPC work versus Machine Learning versus Deep Learning
Modular applications that run instances on Enterprise are generally tuned to run differently than they might be on an HPC system that is running tightly-coupled applications.
  An Enterprise system might require more modular deployment of web services, PAAS, data bases, etc.
  HPC systems might be deploying applications running MPI
  Enterprise workloads, modern HPC problems
One construct that is common to both computing environments is communication and binding of resources----how can me make things simpler?
  Heterogenous deployment of memory, accelerators, such as GPUs, FPGAs, new CPUs that are designed to run specific tasks, NUMA, etc

## Slide 4: This Creates Problems in Manageability
Administrative Management Challenges
No common fabric manager interface or fabric model available to link applications with remote resources
Workload management and optimization is different for each type of fabric
Administrators are being asked to manage an increasing heterogenous fabrics infrastructure, each with its own management standard and model
Fabric Services
Slurm
User APPs & Libraries
Gen-Z
Fabric Manager
Gen-Z
HW
Fabric Services
IB
Ethernet
…
Ethernet
Fabric Managers
Eth
HW
IB
Fabric Manager
…
Fabric Manager
IB
HW
…
HW
Fabric Services
AWS
PBS
Kubernetes
Orchestration Managers
Proprietary
Fabric Manager
AWS
HW
…
…
…
Ethernet
TBD
Fabric Managers
TBD
HW
Fabric Services
Gen-Z
Fabric Services
Fabric Services
Notes: Compute platforms largely have static control and access for fabrics because dynamic control is too difficult to manage for a Complex array of high-speed specialty fabrics
We want to create tools that will work together
Works with the vendor-provided fabrics
Shortens the learning curve with a published API for clients and vendors to be able to work with
Tools that will work together
Control simplicity
This BoF seeks Use-Cases for managing fabrics from the HPC network, storage, and security communities, as well as, open development participation in the OpenFabrics Management Framework. -----what purpose is this for? A new common management framework could provide----why is this true?-----is there a framework at all? Does every vendor provide
Tools will work together
Manager with a published API
Heterogeneous
Control simplicity
More and more diversity in fabrics
A common fabric manager framework could significantly improve performance and simplify control

## Slide 5: The Fabric Admin Services offered by the OFMF
Fabric Services
The Open Fabric Management Framework
  Control Services
    Discovery
    Inventory
  Communication Services
    Connection management
      App to app, manager to manager
    Address Vectors
      Managing fabric addresses
  Partitioning Services
    Zones (subnets, vLans)
    Connections (permitted paths)
    Permissions
  Messaging Services
    Queues and contexts
    Events and errors
    Atomics and other synchronizations
  Security
Slurm
User APPs & Libraries
Gen-Z
Fabric Manager
Gen-Z
HW
Fabric Services
IB
Ethernet
…
Gen-Z
Ethernet
Fabric Managers
Eth
HW
IB
Fabric Manager
…
Fabric Manager
IB
HW
…
HW
Fabric Services
Fabric Services
AWS
PBS
Kubernetes
Orchestration Managers
Proprietary
Fabric Manager
AWS
HW
Open Fabric Management Framework Interface
Notes: Currently the OFMF working group is grinding through use cases associated with building ‘clusters’ (Slingshot and Kubernetes, IB coming) via ‘zones’, and deploying workloads from SLURM and Kubernetes via ‘connections’
During the use case walk throughs we note where OFMF services are going to be needed, and in which format the arguments are likely to be available
Basically working towards a list of the API calls needed northbound of the OFMF, and how they have to look to the fabric specific providers
Thus, the Redfish models are being defined / refined in parallel with the required services
So, the three activities strive to implement this vision as so:
The CXL/Gen-Z bridge defines the fabric features we need for MDC and how the features are mapped into a fabric manager or application node’s working space (at the bottom of the stack, the HW/FW-SW interface)
The Redfish fabric extensions allow the MDC fabric features to be modeled, and thus conveyed and controlled
The OFMF defines the generic fabric services interfaces/APIs to the upper layer tools, resource managers, and apps / libraries and the internal APIs for the fabric specific plugins

## Slide 6: Goals for a Fabric Manager
Create a common set of fabric tools
Support multiple fabric types
Uniform Management
Common monitoring tools
More options for fabric orchestration
Workload Management optimization

## Slide 7: The OpenFabrics Management Framework Architecture
Administration Domain
abstract
manipulations
SLURM
Kubernetes
Framework
OFMF Domain
Hardware
Partition Mgmt
Events & Logs
Authentication
Peer Address Lookup
Gen-Z
Agent
Slingshot
Agent
IB
Agent
Create Zone
Create Zone
Redfish
Model
Native
Model
Create Zone
libfabric
openFAM
Application Domain
Create zone
FAM Resource
Manager
Clients
attach shared memory region
create shmem region
Gen-Z Zephyr FM
Slingshot
FM
IB
SM
MPI
Network knowlege
CXL
Agent
CXL
FM
Create Zone
Notes: Left side is the user/admin/orchestration/automation domain(s)
Right side is the hardware that makes up the fabric and the resources that are accessed thereon
The middle is a representation of the functional blocks making up the OpenFabrics Fabric Management Framework
On the left, various workload managers and app/resource manager libraries are represented. They are all clients
Any entity (SW tool, admin GUI, shell script via CLI) may need to create a virtual platform, pod, cluster, partition, vLan, job queue, subnet or other name for a set of resources that are connected together to enable some workload(s) to execute while being isolated from other jobs.
Such an entity needs a common taxonomy for describing the resources needed in the set and how the connections among them are to behave.
We are proposing to use the DMTF’s Redfish standards to model the fabric and its resources, and to provide the RESTful interfaces through which the entities on the left can learn of the modelled resources and create such a set of fabric resources.
Redfish currently has an object called a ‘zone’ that contains a list of the fabric endpoints which may be connected to each other. Zones can be used to enumerate the members of a vLAN, or the resources of a virtual platform.
Entities on the left hand side make a common call to create a Redfish ‘zone’.
The framework will update the Redfish model for the given fabric(s) and exchange the appropriate details with the fabric specific provider(s)
The Providers are responsible for updating any native models they maintain of their fabric and to issue the appropriate traffic to the fabric hardware
It is important to note that ‘admin tools’ are not the only clients of the OFMF services.
Applications will need runtime support in the form of creating, registering, attaching, and freeing shared memory regions.
OS and virtual machine managers will need an interface to request initial (boot time) resource allocations and runtime changes

## Slide 8: Redfish-Swordfish / OFMF Fabric Model Example
1
Zones
Fabrics
Gen-Z
Navigation Link (odata.id)
singleton resource
Subordinate object
collection resource
Address Pools
AP1
Target
Endpoint
Endpoints
Chassis
1
Memory
ServiceRoot
Account
Service
Session
Service
Event
Service
Update
Service
Telemetry
Service
Manager
Media
Controller
Systems
1
Fabric Adapter
1
1
Initiator
Endpoint
1
Memory
Domain
1
Connections
Conn1
Memory
Chunks
Chunk1
Chunk2
Chunk3
Chunk4
Composer
Notes: This is a scary slide … normally I need 45 minutes to walk through the animations that tell the story of how we use Redfish to create a common fabric model and manage fabrics with it. Today, going to cover just the green objects, in five minutes
Well, we DO Need a common model of a memory semantic fabric with disaggregated, shared resources (memory) for all the upper level tools and libraries to work with…
Let’s take a quick look at how our Redfish fabric model can be useful to a Composing tool
First, this is the Redfish ‘logical view’ of fabric resources and their logical relationships to each other (no physical details like switches  )
A large memory region, say our 1 PB region, can be aggregated together out of 2x 512 TB ‘memory chunks’
Redfish has the memory chunk objects already in place because they were discovered and enumerated prior, but they are not yet composed until we create the ‘logical memory region’.
A 500 node cluster can be created by pulling in the 500 initiator endpoints (fabric bridges on the 500 hosts) into a single ‘zone’.
The memory chunks that make up the ‘logical memory region’ are also placed into the same zone.
The endpoint objects all exist because they were already discovered, but they are not collected together into a cluster or ‘zone’ so they are just disaggregated resources.
Once the 500 initiator endpoints are in the same zone as the memory chunks, the fabric specific manager can program routes through the switches. The fabric will now allow these endpoints to pass packets through the switches to each other.
However, endpoints are not yet enabled to send or receive packets until a connection is made.
Connections can be made between each host (initiators) and the multiple targets (memory chunks) that make up the logical memory region. That gives all the hosts simultaneous access to the 1 PB memory region.
However, if all host to host communication is expected to be done through shared FAM mailboxes, there should be no connections directly between hosts.
Thus, Connections enable endpoints to send or receive packets independently of whether the switches will route the packets. This is a requirement of Gen-Z’s asymmetric connection privileges.
This is how Redfish solves our common fabric model, common fabric services interface problem.