## Slide 1: Proof-of-Concept Fabric Agent using Gen-Z

## Slide 2: OFMF Redfish Tree: Consolidated Physical Objects, Endpoints, and Port linkages
Fabrics
Gen-Z 1
Navigation Link (odata.id)
singleton resource
Subordinate object
collection resource
Endpoints
ServiceRoot
Systems
1
1
2
Chassis
1
Media
Controller
Memory
Domain
1
5
4
Fabric Adapters
1
Fabric Adapters
1
Ports
1
1
2
3
1
2
Switches
SW1
Ports
1
2
3
4
5
6
1
3
2
7
6
3
5
7
6
4
1
2
Ports
1
Ports
1
Ports
1
2
Navigation Link representing physical
Fabric links (always between ports)
Navigation Links between Redfish models
3
Fabric Adapters
1
3
4
Ports
1
2
3
4
3
3
1
2
4
2
2
7
8
2
Ports
1
2
Ports
1
2
Connections
1
Memory
Chunks
Chunk1
Chunk2
3
4
3
4
3
4
3
4
SoC
SoC
FM

## Slide 3: Redfish Physical Fabric Model
Systems
1
Insights
Fabric itself (the connectivity) is modeled as ports and endpoints
Physical fabric connections (eg. Cables) are always between ‘Ports’
Ports are traced back to the fabric devices that drive the ports
Fabric devices trace back to physical or logical infrastructure (what controls the fabric device) AND to the ‘Endpoint’ object associated with the fabric device
Discovery of physical and logical resources accessible via the fabric is a fabric-specific operation.
Non-fabric resources (those not directly visible to the fabric) associated with the fabric devices ( the fabric endpoints) may or may not have detailed Redfish models and schema that can be accessed via the same Service Root.
For example, if the ServiceRoot shown is maintained by the ‘fabric manager’, the fabric manager may not have any visibility to details about ‘System 3’ behind the fabric adapter.
The fabric manager must know sufficient details about the fabric adapter to correctly enable the system to access those other endpoints on fabric the server is allowed to reach.
Endpoints
1
Switches
SW1
Fabric Adapters
1
Ports
1
2
Ports
1
2
6
3
3
Ports
1
2
3
4
5
6
3
8
9
a
b
ServiceRoot
<FabricType>
Navigation Link representing physical
Fabric links (always between ports)
Navigation Links between Redfish models

## Slide 4: Redfish/Swordfish Hierarchy: Extending Fabric Management
Redfish/Swordfish
NVMe

## Slide 5: Use-Case Descriptions
Use Case Description | Fabric Resource Hot Add
Actors | OFMF Fabric Manager, Administrator, Fabric Subnet Manager
Description | Add components when detected by a Subnet Manager
Normal Flow | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabri A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric • The Subnet Manager identifies a previously identified endpoint through a UID The Subnet Manager provides a fabric-specific identifier The Subnet Manager communicates to the Agent that an addition has been made to the fabric The Agent notifies OFMF Redfish that a fabric change has occurred The OFMF does a Get to request the Agent to identify the change The OFMF needs to notify the clients of the net impact through an event. The OFMF updates the Redfish tree with the addition of new information using the Redfish Aggregation Service For the POC, the agent can post the information directly to the OFMF instance
Alternate Flow 1 | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric No deletion is identified

## Slide 6: Client POSTs New Connection
Once an appropriate Memory Chunk is available, a client may POST a Connection to it from an SoC
Client POSTs new Connection
  Set initiator endpoints (Fabric Adapter)
  Set target endpoint (Memory Chunk)
OFMF POSTs OFMF object in local tree (pending)
OFMF relays POSTs request to Agent
Agent indexes local DB with Redfish URI to locate FM’s “memory resource” associated with Memory Chunk
  If resource does not exist, Agent returns FAIL
Agent indexes local DB to locate FM’s ‘consumer’ associated with initiator URI of request
  If resource does not exist, Agent returns FAIL
Agent assigns memory resource the proper Consumer description in DB
Agent sends FM (Zephyr) the proper add_resource() command with JSON resource description
Zephyr parses request
  Zephyr routes switch paths
  Zephyr configures initiator and target endpoint components
  Zephyr returns Success
Agent updates local DB status and returns Success to OFMF
OFMF finalizes update of OFMF object in local tree
OFMF returns Success to Client
Search for key=URI in nodes/resources
POST OFMF:/.../Connections/ID
Extract Resource IDs and status
Blue text: blue text are tasks that are fabric manager / Agent specific.
Zephyr must enable both the switch paths and the endpoint firewalls to enable the connection. How to establish Zones separately from Connections with Zephyr / Agent API is TBD
POST Agent:/.../Connections/ID
HTTP Zephyr:/resource/create {}

## Slide 7: Use-Case Descriptions
Use Case Description | Fabric Resource Hot Subtract
Actors | OFMF Fabric Manager, Administrator, Fabric Subnet Manager
Description | Subtract components when is detected by a Subnet Manager
Normal Flow | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric The Subnet Manager finds a missing endpoint The Subnet Manager deletes the endpoint The Subnet Manager communicates to the Agent that a deletion has been made to the fabric The Agent notifies OFMF that a fabric change has occurred The OFMF does a Get to request the Agent to identify the change The OFMF updates the Redfish tree with the deletion through a post of new information or delete OFMF reports to clients that a modification to the fabric has occurred.
Alternate Flow 1 | A periodic Subnet Manager sweep recursively performs a scan of it’s currently running fabric No deletion is identified

## Slide 8: Link has gone down Use case description
Use Case Description | Resource has gone down Use-Case description
Actors | Agent, Subnet Manager, OFMF
Description | Delete an identified resource from the OFMF
Comments | A resource has been cancelled and the resource is to be deleted to the OFMF
Input Data | Fabric Attached components/resources are matched to a consumer Resource characteristics, type of resource, address range, UUID and serial number Configuration restriction decides who can connect/bind to what resource, no randomness
Preconditions | Redfish contains information on resources Resources are available and online Subnet Manager is in operation Subnet Manager is parsing the underlying fabric
Postconditions | Resource Manager will return to the Composability Manager a Redfish object URI to a logical resource that it deleted in the Redfish tree
Trigger | Resource Manager detects a change in the fabric and that a resource was lost/eliminated through an Unsolicited Event Packet (UEP)
Normal Flow | Resource Manager parse the request Resource Manager polls it’s inventory If it has a matching resource, then it returns the Object URI that provides the OFMF with information on the missing resource.
Alternate Flow 1 | Resource Manager parse the request Resource Manager polls it’s inventory It finds the matching resource The Redfish tree is updated
Alternate Flow 2 | 

## Slide 9: Create a Fabric attached memory block
Use Case Description | Create a Fabric Attached Memory Block
Actors | Composability Manager, Resource Manager, OFMF
Description | Provide attached memory block
Comments | Assume that the Resource Manager is provided with information to make a good choice Amount of Resources are available
Input Data | Requirements for memory from the template from the platform
Preconditions | Redfish contains information on memory resources Resources are available and online Resource Manager has already queried Redfish for resources
Assumptions | We will have memory devices subdivided into 4 components. We can distribute the 4 components, as necessary We can aggregate portions of the 4 components. No interleave support for the SC21 demo.
Postconditions | Resource Manager will return to the Composability Manager a Redfish object URI to a logical resource that it created in the Redfish tree that meets the Zone need.
Trigger | Composability calls the Resource Manager and requests memory
Normal Flow | Resource Manager parse the request Resource Manager polls it’s inventory If it has a matching resource, then it returns the Object URI that meets the Zone need.
Alternate Flow 1 | Resource Manager parse the request Resource Manager polls it’s inventory It does not have a matching resource Resource Manager (RM) queries unallocated memory RM creates a memory chunk using the URI of the appropriate unallocated memory A Region Object contains a chunk object If it has a matching resource, then it returns the Object Region URI that meets the Zone need.
Alternate Flow 2 | Resource Manager parse the request Resource Manager polls it’s inventory It does not have a matching resource Resource Manager (RM) queries unallocated memory RM determines a needs for a region of memory chunks RM creates memory regions using the URIs of the appropriate chunks to provide access to unallocated memory The RM calls the OFMF and create a region of memory chunks using the underlying devices A Region Object contains a multiple chunk objects If it has a matching resource, then it returns the Object Region URI that meets the Zone need.

## Slide 10: Client POSTs New Memory Chunk
Since initial configuration created 1 Memory Chunk for every Media Controller (zMM), clients must first modify or delete the original memory chunk before a new one can be defined within the original Memory Domain/Media Controller
Client GETs appropriate memory objects
Client POSTs new Memory Chunk
  Set size
  Set starting address
OFMF POSTs OFMF object in local tree (pending)
OFMF relays POSTs request to Agent
Agent indexes local DB with Redfish URI to locate FM’s “memory resource”
  If resource exists, Agent returns FAIL
  If resource does not exist, Agent appends new resource
Agent assigns memory resource description in DB
  Resource has no consumers (it is un-used still)
  Agent verifies start address and size are valid!
  Agent returns Success
  Agent does not update Zephyr
OFMF finalizes update of OFMF object in local tree
OFMF returns Success to Client
GET OFMF:/.../Memory...
Search for key=URI in nodes/resources
POST OFMF:/.../MemoryChunks
Extract Status
In Use = linked to “consumer”
Classify and cataloge Nodes
Blue text: blue text are tasks that are fabric manager / Agent specific.
Zephyr can only be updated about active memory resources (producers), which are those with ‘connections’ (IE, with associated consumers)
POST Agent:/.../MemoryChunks

## Slide 11: Client PATCHes Memory Chunk
Since initial configuration created 1 Memory Chunk for every Media Controller (zMM), clients must first modify or delete this original memory chunk
Client GETS appropriate memory objects
Client PATCHes initial Memory Chunk
  Set size to smaller amount
  Possibly set new starting address
OFMF updates OFMF object in local tree (pending)
OFMF relays PATCH request to Agent
Agent indexes local DB with Redfish URI to locate FM’s “memory resource”
  If resource exists and is in use, Agent returns FAIL
  If resource does not exist, Agent returns NOT FOUND
Agent updates memory resource description in DB
  Agent does NOT update Zephyr
  Agent returns Success
OFMF finalizes update of OFMF object in local tree
OFMF returns Success to Client
GET OFMF:/.../Memory...
Search for key=URI in nodes/resources
PATCH OFMF:/.../MemoryChunks
Extract Status
In Use = linked to “consumer”
Classify and catalogue Nodes
Blue text: blue text are tasks that are fabric manager / Agent specific.
Agent does not update Zephyr about changes to un-used memory chunks since Zephyr does not track them (?)
PATCH Agent:/.../MemoryChunks

## Slide 12: Populate Initial Config in POC
Start the OFMF service
Initial Configuration is empty tree---flush the database
OFMF Connects to FM agent
  PoC: Hardcode all HTTP connections
  Some form of initial handshake
Agent will locate the FM (Zephyr)---make a request call, in Python with a timeout (5s configurable default) looping request
Agent requests Zephyr fabric config
  Zephyr returns NetworkX graph in JSON
Agent interprets the NetworkX graph
  Agent ‘sucks in’ the NetworkX JSON with 1 NetworkX call
  Then, Agent does a variable for loop on nodes,edges, etc.
  Nodes are Switches, Fabric Adapters, or Media Controllers
Agent creates DB of these objects, indexed by Zephyr ID
  Maps Redfish schema to node descriptions
  Adds implied ‘memory resources’
Agent POSTS appropriate objects to OFMF
  Nodes posted to OFMF
    Media controllers are 1 Memory Domain
    Memory Domains imply 1 Memory Chunk
    Memory Chunk = Zephyr ‘memory resource’
  Fabric links inserted
  Default Zone?
  Default FM Connections
Agent updates local DB to add OFMF URI for nodes
  Agent is responsible for maintaining the mapping between OFMF and Zephyr object names
HTTP (GET) Zephyr:/topology
POST OFMF:/redfish/.../connections
POST OFMF:/redfish/v1/xxx
Parse NetworkX JSON
Default Zone does not create switch paths in Zephyr’s fabric
List of Fabric links
List of Fabric Components (Nodes)
POST tree framework
Classify and catalogue Nodes
Blue text: blue text are tasks that are fabric manager / Agent specific.
Zephyr initial config establishes only connections between FM and each in band managed component
POST nodes & required subordinates
PATCH nodes with navigation to ports
Append physical nodes to DB
Create new ‘memory resources’ as appropriate
POST OFMF:/redfish/v1/xxx

## Slide 13: Boundaries
Responsibility of the Agent
  Notify OFMF of changes of fabric endpoints, switches and FAM
    Event interface
  Support standard Redfish
    Post, Patch, and Delete only for POC
  The Agent needs to use Simple Service Discovery Protocol (SSDP)
    We will determine for the POC the amount of time/work available
Security Concerns
  How much of the Redfish Aggregation model do we follow?
    We need to decide whether to support Session+ authentication
  Clients cannot interact in its roll with the Agents
Limits of the Agent
  Will interact with the Subnet Manager
  Will interact with the OFMF
    Changes will be made directly to Redfish
  OFMF Clients cannot interact with the Agents directly
  Agents cannot control the fabric infrastructure -–Subnet Manager responsibility

## Slide 14: Agent Flow diagram for POC
Actions | Attributes
Agent launches on in daemon mode as a co-application to the Subnet Manager POC Zephyr has a Grand Plan spec to launch the Agent | Who the Agent is How to turn on Agent Path location of Agent
Agent locates Subnet Manager and turns it’s ears on | Flag for insertion/deletion Identifier to component Wiring points
Locate the OFMF using SSDP | Service Identifier(s) OFMF Acknowledgement
Agent receives a notification from the Subnet Manager | Add/Delete event Add/Delete flag Fabric-specific object description
Agent sends a Redfish event to the OFMF OFMF may respond with a Get to Agent OFMF notifies client(s) | Redfish event Change information
Agent performs a Post/Delete to update the OFMF Redfish Tree | 
Agent performs a Post/Delete to update the OFMF Redfish Tree | Redfish object resource representation(s)
Clients receive information from OFMF Redfish Tree that a change has occurred | Register from Redfish Events from OFMF

## Slide 15: OFMF Functionality needed for POC
Zones
  Default Zone includes everything on fabric
    Agent populates this and adds the FM (optional?)
    Clients cannot manipulate the default zone?
  GET, POST, PATCH (PUT?), DELETE
Connections
  GET, POST, PATCH (PUT?), DELETE
  Agent may populate FM connections
  Clients may not be allowed to see the FM’s connections or zones
Fabric Adapters (hosts, SoCs)
  GET, POST, PATCH (PUT?), DELETE(?)
  Must be associated with ‘systems’
    If associated system is Deleted, OFMF must delete hosted fabric adapters first
  For PoC the Agent or Client POSTs are made to a ‘system’, but such systems contain only Fabric Adapters

## Slide 16: Redfish Objects needed for PoC
Fabric Adapter and ports
  Plus required placeholder ‘system’ path objects and collections
Stand Alone Switch and ports
Media controller and ports
  And associated Memory Domain
  Plus required placeholder ‘Chassis’ path objects and collections
Zones
Connections
  Including Rkeys IFF PoC implements R-Key checking
Address pools -NOT Required
  POC: probably not since FM supplies all fabric addresses when component is discovered
Logical Memory Regions –NOT Required
  Only required if PoC implements zMM memory chunk interleaving or mirroring
Memory Chunks
R-Keys -NOT Required
  See “Connections”
Link-up events (hot add)
  Passed from Agent through OFMF to clients registered for them
Link-dn events (surprise removal)
  Agent should trap planned Link-dn events whenever a resource is programmatically disabled or removed
  POC: Agent can be enabled to forward all Link-up and Link-dn events to clients so apps demonstrating Health Monitoring can show off
Protection violations events
  As available from Hardware
  As forwarded from Zephyr through the Agent to OFMF

## Slide 17: OFMF Functionality needed for POC
Simple GETS on all objects, Register for those Events emitted by object which Zephyr will actually forward (list TBD)
Memory chunks (physical chunks)
  GET, POST, PATCH (PUT?), DELETE
  always a subordinate of a Memory Domain
  Linked to actual Media Controller endpoint through Memory Domain
Media Controller (zMMs)
  GET, POST, PATCH (PUT?), DELETE
  Does NOT spawn a Memory Domain
    Client or Agent must POST the associated Memory Domain
Memory Domain
  GET, POST, PATCH (PUT?), DELETE
  Must be linked to Media Controller
  If Media Controller is DELETED, the Memory Domains must go away
Stand-Alone Switches
  GET, POST, PATCH (PUT?), DELETE(?)
  Agent POSTs and DELETEs standalone switches and associated Ports
    Routing tables are ‘fabric specific’
    Routing tables values are not visible to clients & OFMF?
  App clients don’t manipulate switches?
    May need to have visibility on them
  Routing table values are not visible to clients
    Should not need to support table data in OFMF of POC
Integrated switches are part of Media Controllers or Fabric Adapters
  Manifest as resources under Ports structures
  Routing tables associated with ports are fabric specific
  Routing table values may not be visible to clients
    Should not need to support table data in OFMF of POC

## Slide 18: Zephyr SM Launch
Json formatted configuration file
Zephyr does a discovery and resource descriptions from a static file in SM node
  Fabric Attached components/resources are matched to consumers
  Resource characteristics, type of resource, address range, UUID and serial number
  Configuration restriction decides who can connect/bind to what resource, no randomness
  Wiring-–Python NetworkX to communicate wiring topology, potential wiring pathway that could be used.
  Flags---for driver
Zephyr listens for Agent-–policy not determined---cURL--(HTTPS, web interface)
Dump available resources
    Fabric Attached components/resources, as producers, are matched to consumers
    Resource characteristics, type of resource, address range, UUID and serial number
    Configuration restriction decides who can connect/bind to what resource, no randomness
Connection binding restrictions and hops

## Slide 19: Zephyr SM Launch
What is the information?
Producers and Consumers
Nodes and Edges
Associations that provide Zones
  After PoC—Rkey security

## Slide 20: Agent Meet Subnet Manager--Zephyr
Redfish Database
Reach out to Zephyr to gather resource information and policies using cURL and HTTP-FLASK
  Receive available resources
    Fabric Attached components/resources are matched to a client
    Resource characteristics, type of resource, address range, UUID and serial number
    Configuration restriction decides who can connect/bind to what resource, no randomness
    Connection binding restrictions and hops
  Filling the Redfish/Swordfish database using Posts or Deletes
  Patches for Zones

## Slide 21: Agent receives update from Zephyr
Agent receives an event notification---RPC call?
Zephyr listens for Agent-–policy not determined---cURL--(HTTPS, web interface)
Dump what changed?
    Fabric Attached components/resources are matched to a consumer
    Resource characteristics, type of resource, address range, UUID and serial number
    Configuration restriction decides who can connect/bind to what resource, no randomness
Connection binding restrictions and hops
Create the objects
Define the links to objects
Create the zones starting with the overall default fabric zone after the bindings are created

## Slide 22: Agent Flow diagram
Actions | Attributes
Agent launches on in daemon mode as a co-application to the Subnet Manager POC Zephyr has a Grand Plan spec to launch the Agent | Who the Agent is How to turn on Agent Path location of Agent
Agent locates Subnet Manager and turns it’s ears on | Flag for insertion/deletion Identifier to component Wiring points
Locate the OFMF using SSDP | Service Identifier(s) OFMF Acknowledgement
Agent receives a notification from the Subnet Manager | Add/Delete event Add/Delete flag Fabric-specific object description
Agent sends a Redfish event to the OFMF OFMF may respond with a Get to Agent OFMF notifies client(s) | Redfish event Change information

## Slide 23
change
Yes
No
SM Launch
Recursively walk the fabric
Listen for OFMF Agent
Resources
Agent Launch
Load configuration file
Who the Agent is
How to turn on Agent
Path location of Agent
Agent meet SM
Agent locates Subnet Manager and turns it’s ears on
Flag for insertion/deletion
Identifier to component
Resouce Attachments
Agent locate OFMF
Locate the OFMF using SSDP
Service Identifier(s)
OFMF Ack
Subnet Manager
Recursively walk the fabric
Endpoints
Switches
SM Notification
Subnet Manager notifies Agent
Add/Delete event
Add/Delete flag
Fabric-specific obj desc
Agent Receives Update
Agent receives a notification from the Subnet Manager
Agent Redfish Update
Agent sends a Redfish event to the OFMF
OFMF may respond with a Get to Agent
OFMF notifies client(s)
Redfish event
Change information
Add/Delete event
Add/Delete flag
Fabric-specific obj desc

## Slide 24: What Resources
Discover
Topology
Turn on HTTPS
Turn on Agent
Access to Zephyr?
Hold for 5s
No
Get Resource and NetworkX info
Yes
Provide Resource and NetworkX info
Translate to Redfish
Response from clients?
Translate to JSON
Execute changes
Hold for 5s

## Slide 25: Subnet Manager Run-time maintenance mode
Subnet Manager notifies Agent that an addition/subtracton has been made
change
Yes
No
OFMF Updates the clients that a change has occurred
Update the Redfish Tree with the Addition/Deletion
Agent sends change information using a OFMF Redfish event mechanism POC Post/Delete
Recursively walk the Fabric
Load Configuration File
Maintain current state
OFMF does a Get to the Agent to identify the fabric change

## Slide 26: Zephyr Events
Here's the list of notifications that zephyr can (currently) send to higher-level managers:
1. component add
2. component change
3. resource add
4. resource add-consumers
5. resource remove
6. resource remove-consumers
7. new PFM
8. new SFM
9. SFM to PFM promotion
10. routes add
11. routes remove
12. interface change

## Slide 27: Agent
Python 3.6 and above
Python does Flask and Rest interfaces well
Python processes JSON well
Gen-Z Zephyr operates with 2 node UUIDs, 1 is permanent, 1 is ephemeral
Edge connections match to ephemeral UUIDs on NetworkX
Naming scheme in Redfish?
Zephyr doesn’t want to know what is happening at the Redfish layer and above.
Now, I need to tell Zephyr about the new object in the fabric and what to do with it with a Put.
Zephyr does not do a periodic scan. So, objects added must be conveyed and explained to Zephyr.
  Connections to the new added object
  Zephyr will retrieve the permanent UUID from the new added object.
  Zephyr will assign an ephemeral UUID to the new added object.
  Redfish can assign a user-friendly name to the new added object above Zephyr?
  Zephyr could/and can use the user-friendly names, from Redfish in it’s low-level tools.
    #> lsgenz could use the user-friendly names for System Admin help

## Slide 28
Get Collections
Get Connections
Get Fabric Instance
Get Fabric Adapters
Get Fabric Adapter Ports
Get Chassis Instance
Get Media Controllers
Get Media Controller Ports
Get Chassis Memory Domain
Get Switches
Get Fabric Switch Ports
Get Endpoints
Get MD Chunks
Fabric Add Resource
Add Database Link

## Slide 29: Agent Top-Down design- Event Manager
Event Manager Service Events signal changes in fabric
Maintain Current State/Intended State/Health State
Map changes to OFMF representation

## Slide 30: Agent Top-Down design
Agent
OFMF Redfish Communicator
Subnet Manager Interface
Event Manager Service Events signal changes in fabric

## Slide 31: Subnet manager scan and modify OFMF redfish
OFMF
Agent 2
Agent 3
Agent n
Agent 1
Subnet Manager
Subnet Manager can talk to 1 or more Agents

## Slide 32: Agent/OFMF initial configuration-–Part 1
Initial Configuration of SM
Retrieve full report back in JSON of Fabric from Zephyr
Retrieve topology back in NetworkX
Report initial configuration to OFMF in Redfish
Translate Fabric and topology to Redfish
Health characteristics

## Slide 33: Agent top-down design-Subnet Manager Interface
Subnet Manager Interface
Translates between SM protocol and OFMF protocol
Initial Configuration of SM
Current State
Reading initial state of the SM

## Slide 34: Agent/OFMF initial configuration-–Part 2
34
Retrieve full report back in JSON of Fabric from Zephyr
Retrieve topology back in NetworkX
Report initial configuration to OFMF in Redfish
Redfish required properties---Redfish port descriptions, Id's and names will need to be mapped in POST
@odata.id, @odata.type, Id, Name
UUID,, serial number, resource characteristics, address range
Translate Fabric and topology to Redfish
Port to port links that are active, endpoints, cable characteristics
Overall status, optional fields, Redfish navigation links, ports up/down, link speed, flap
Health characteristics

## Slide 35: Agent Top-Down design- Event Manager
Event Manager Service Events signal changes in fabric
Maintain Current State/Intended State/Health State
Map changes to OFMF representation

## Slide 36: Agent top-down design-Link has been established
Link has been established.
What resource?
Unsolicited Event Packet (UEP)
JSON representation of the fabric
UUIDs for new resources
New route information

## Slide 37: Get Zephyr Config
Create a Post to Zephyr a request for /fabric/topology
Zephyr UIR is g.Zephyr
Get Request from Zephyr
Get returned r.json as a data file
If g.ZEPHYR is NONE
No Zephyr is Default File returned
Zephyr Exists and We need the topology
Zephyr Doesn’t Exist We need no topology

## Slide 38: Is Object Modified?
Acquire Old Object and New Object from Pass In
Check the MOD Timestamp New is newer than OLD?
Return True
Return False
Does MOD timestamp exist in both OLD and New?
No
Yes
Yes
No

## Slide 39: Update Zephyr Node IDs
The Agent Node ID is set to the Instance UUID
Recursively copy in all of the Node IDs
Recursively copy in all of the c_UUIDs
Recursively copy in all of the Serial Numbers
Redfish UUIDs
Node Enabled?
Get Memory Chunk Info
Is Node the PFM Fabric Manager?
Designate Info for Node as the PFM
Split the Node info into objects
Yes
Designate Node as Enabled
Designate Node as disabled
Yes
No
Return the Changes

## Slide 40: Update Agent Node Ports
Localportconfig
peerportconfig
agentconfig
Get the local port numbers
Check for an update request using Is_Object_Modified?
Get the local and peer port numbers
Is the local port in our list?
Yes
Update Ports
Make a new port
No
Copy in node info
Create a Redfish Number

## Slide 41: Parse Zephyr Link
agentConfig
zNodeLink
Build a nodeIDList &
nodeList
Call
Update Agent Node Ports with the ends of the link

## Slide 42: Upload Fabric Instance
Get All of the Agent nodes
Get Fabric Instance
Insert fabric UUIDn into Redfish

## Slide 43: Upload Chassis
allAgentNodes
memDomainCount
Chassis ID
Append Chassis to Nodes
Post to Redfish

## Slide 44: Create Redfish IDs
allAgentNodes
cClassDecoder
Memory
IDs
Bridge
IDs
Switch
IDs

## Slide 45: Post Redfish Nodes
allAgentNodes
cClassDecoder
Post Memory
Controller
Nodes
Post Fabric Adapter Nodes
Post Switch Nodes

## Slide 46: Create Fabric Adapter IDs
allAgentNodes
NodeID
Post new ID
Get a Redfish ID

## Slide 47: Update Media Controller Node IDs
allAgentNodes
NodeID
Post new ID
Get a Redfish ID

## Slide 48: Create Switch IDs
allAgentNodes
NodeID
Post new ID
Get a Redfish ID

## Slide 49: Create Memory Chunk IDs
Chassis Memory Domain Instance
Media Controllers
Media Controllers
Minimum and Maximum Memory Size
Start and Stop Memory Position
Zephyr Node ID

## Slide 50: Post Fabric Adapter Nodes
allAgentNodes
NodeID
Zephyr Node Ids
Redfish Ids
Get Computer System ID
Details: MinChunkSize
MaxChunkSize
Endpoints
allAgentNodes

## Slide 51: Post Fabric Adapter Nodes
allAgentNodes
NodeID
Zephyr Node Ids
Redfish Ids
Get Computer System ID
Details: MinChunkSize
MaxChunkSize
Endpoints
allAgentNodes

## Slide 52: Post Switch Ports
allAgentNodes
NodeID
Zephyr Node IDs and Switch Port IDs
Redfish Ids
Get Computer System ID
Details: MinChunkSize
MaxChunkSize
Endpoints
allAgentNodes

## Slide 53: Create Root Collections
Ctype is Chassis
cType is Fabrics
cType is Systems
Redfish root path is: /redfish/v1
Path is /redfish/v1/Systems
Path is /redfish/v1/Fabrics
Path is /redfish/v1/Chassis
getCollectionInstance for
Systems
/redfish/v1/Systems
getCollectionInstance for
Fabrics
/redfish/v1/Fabrics
getCollectionInstance for
Chassis
/redfish/v1/Chassis
Post the file
Post the file
Post the file

## Slide 54: Post to OFMF
allAgentNodes
Post
resetgenz
Post
@odata.id