## Slide 1
GenZ Switch with GenZ to CXL Adapter
CXL 1.1 to GenZ Host Adapter with Integrated Switch
NIC
Resource Enclosure 1
GenZ Switch
GenZ Top Of Rack Switch
Composable Resource Pool Collections
Composed Server Collections
GPU
Composed server 1
x86 CPU
x86 CPU
PCIe to GenZ Host Adapter with Integrated Switch
Composed server 2
x86 CPU
x86 CPU
NVMe to GenZ Host Adapter with Integrated Switch
Composed server 3
x86 CPU
x86 CPU
FPGA SOC + GenZ IP (including integrated switch)
Composed server 4
ARMCPU
DDR
DDR
SSD
SSD
DDR
DDR
SSD
SSD
DDR
DDR
SSD
SSD
DDR
SSD
ASIC with Integrated GenZ IP (including integrated switch)
Composed server 4
Risc-V CPU
DDR
SSD
GenZ (including integrated switch)
Composed server N
CPU
DDR
SSD
NIC
Primary Fabric Manager
Secondary Fabric Manager
Orchestration Server
CPU
NIC
OFMF
Orchestrator (Grand Plan)
Other Fabrics
GenZ Top Of Rack Switch
GenZ Top Of Rack Switch
GenZ Top Of Rack Switch
Ethernet Switch
GenZ FAM
Resource Enclosure 2
CXL SLD
CXL SLD
CXL SLD
GPU
GPU
GenZ Switch with GenZ to PCIe Adapter
GPU
Resource Enclosure 3
NVMe SSD
NVMe SSD
NVMe SSD
GPU
GPU
GenZ FAM
GenZ FAM
GenZ FAM
GenZ FAM
GenZ FAM
GenZ FAM
DDR
DDR
DDR
DDR
DDR
DDR
DDR
DDR
Fabric Manager to OFMF
component add
component change
resource add
resource add-consumers
resource remove
resource remove-consumers
OFMF to Fabric Manager
Topology and component descriptors
Resource to host assignment/de-assignment/reassignment
new PFM
new SFM
SFM to PFM promotion
routes add
routes remove
interface change
Notes: CXL-3.0 is peer-to-peer. If you think about it, peer-to-peer connections can allow you to resources and all of the resources connected to the CXL switches are equally available to each node. In this example I can share GPUs connected to the swtiches, even in separate boxes CPUs, memories. Further, with management, I can reach across this RDMA fabric and switch, and more remotely pull in resources, in an emergency. Sometimes applications can run the nodes out of memory. In another example, I might have oversubscribed a physical node with too many containers. In another example, parallel IO servers might be overloaded. Lustre often uses Z-Pools and ZFS Adaptive Replacement Caches (ARC) caches can be suceptiable to overfilling and that can cause thrashing. The MDS and/or OSS services can cause Lustre failure.