## Slide 1: Centralized Composable HPC Management with the OpenFabrics Management Framework
SAND2023-03887A
Michael Aguilar
Phil Cayton (Intel), Christian Pinto (IBM), Russ Herrell (HPE)
IPDPS/COMPSYS23
St. Petersburg, Florida, USA
May 19, 2023

## Slide 2: Contributors to the OFMF
The goal of the OFMF is to enable interoperability through common interfaces to enable client Managers to efficiently connect workloads with resources in a complex heterogenous ecosystem, without having to worry about the underlying network technology.

## Slide 3: What are Composable Disaggregated HPC Systems?

## Slide 4: What are Composable Disaggregated HPC Systems?
CPU
CPU
CPU
FAM
MEMORY
FAM
MEMORY
FAM
MEMORY
BLOCK
STORAGE
BLOCK
STORAGE
BLOCK
STORAGE
SPECIFIC OR CONSTRAINED COMPOSITION
Existing Chassis
Existing Chassis
Existing Chassis
FAM MEMORY
BLOCK STORAGE
EXPANDABLE COMPOSITION

## Slide 5: Composable Disaggregated Infrastructure (CDI) in an HPC Architecture
Existing Chassis
Existing Chassis
Existing Chassis
FAM MEMORY
BLOCK STORAGE
SPECIFIC AND EXPANDABLE COMPOSITION
Pools can be used to augment memory with direct-addressable devices and block devices
ccNUMA for the FAM memory
NVMeoF for the Block storage

## Slide 6: What are Composable Disaggregated HPC Systems?
Homogeneous HPC Systems become Heterogeneous HPC Systems

## Slide 7: What are Composable Disaggregated HPC Systems?

## Slide 8: OpenFabrics Management Framework for Composable Distributed Systems
We need a centralized control infrastructure to manage our disaggregated compositions and decompositions
We want:
To be able to control Composable Disaggregated Infrastructure (CDI) in an HPC Architecture
Redfish Representation of a Composable Disaggregated Infrastructure Components. Redfish provides us with structures that we can use to store and read component information.
Swordfish Representation of Storage Pools, Volumes, and Endpoint Groups
A centralized service that can provide current up-to-date information on CDI compositions and cluster state information
A centralized service that can abstractly manage our CDI compositions

## Slide 9: Redfish Representation of a Composable Disaggregated Infrastructure Redfish mapping of a simple HPC system

## Slide 10: Redfish Representation of a Composable Disaggregated Infrastructure Redfish mapping of a simple HPC system
$> curl -X GET -H "Content-Type: application/json" htp://ofmfserv:5000/redfish/v1/Fabrics
{
"@odata.type": "#FabricCollection.FabricCollection",
"Name": "Fabric Collection",
"Members@odata.count": 2,
"Members": [
{
"@odata.id": "/redfish/v1/Fabrics/NVMeoF"
},
{
"@odata.id": "/redfish/v1/Fabrics/Ethernet"
}
],
"@odata.id": "/redfish/v1/Fabrics"
}(Swordfish)
curl -X POST -H "Content-Type: application/json" -d @fabric_connection.json http://ofmfserv:5000/redfish/v1/Fabrics/CXL
Warning: Couldn't read data from file "fabric_connection.json", this makes an
Warning: empty POST.
{
"@odata.id": "/redfish/v1/Fabrics/CXL",
"@odata.type": "#Fabric.v1_3_CXL.Fabric",
"Id": "CXL",
"Name": "Fabric"
}

## Slide 11: Redfish Representation of a Composable Disaggregated Infrastructure Redfish mapping of a simple HPC system
curl -X GET -H "Content-Type: application/json" htp://ofmfserv:5000/redfish/v1/Fabrics/NVMeoF/Endpoints/Initiator1
{
"@odata.type": "#Endpoint.v1_7_0.Endpoint",
"Id": "Initiator1",
"Name": "NVMe-oF Initiator (Host)",
"EndpointProtocol": "NVMeOverFabrics",
"Identifiers": [
{
"DurableName": "host.corp.com:nvme:nvm-subsys-sn-4635",
"DurableNameFormat": "NQN"
}
],
"ConnectedEntities": [
{
"EntityType": "NetworkController",
"EntityRole": "Initiator"
}
],
"IPTransportDetails": [
{
"TransportProtocol": "Ethernet",
"IPv4Address": {
"Address": "10.3.5.205"
},
"Port": 13244
}
],
"Links": {
"Connections": [
{
"@odata.id": "/redfish/v1/Fabrics/NVMeoF/Connections/1"
}

## Slide 12: Redfish Representation of a Composable Disaggregated Infrastructure Redfish mapping of a simple HPC system
curl -X GET -H "Content-Type: application/json" http://ofmfserv:5000/redfis/v1/Fabrics/NVMeoF/Connections/1
{
"@odata.type": "#Connection.v1_0_0.Connection",
"@Redfish.ReleaseStatus": "WorkInProgress",
"Id": "1",
"Name": "Host Connection 1",
"Description": "Connection info for host 1",
"ConnectionType": "Storage",
"VolumeInfo": [
{
"AccessCapabilities": [
"Read",
"Write"
],
"Volume": {
"@odata.id": "/redfish/v1/Storage/IPAttachedDrive1/Volumes/SimpleNamespace"
}
},
{
"AccessCapabilities": [
"Read",
"Write"
],
"Volume": {
"@odata.id": "/redfish/v1/Storage/IPAttachedDrive2/Volumes/SimpleNamespace"
}
}
], }
]
},
"@odata.id": "/redfish/v1/Fabrics/NVMeoF/Connections/1"

## Slide 13: Redfish Representation of a Composable Disaggregated Infrastructure CXL-3.0

## Slide 14
curl -X GET -H "Content-Type: application/json" http://ofmfserv:5000//redfish/v1/Storage/IPAttachedDrive2/Volumes/SimpleNamespace
{
"@odata.type": "#Volume.v1_8_0.Volume",
"Id": "1",
"Name": "Namespace 1",
"LogicalUnitNumber": 1,
"Description": "A Namespace is a quantity of non-volatile memory that may be formatted into logical blocks. When formatted, a namespace of size n is a collection of logical blocks with logical block addresses from 0 to (n-1). NVMe systems can support multiple namespaces.",
"Status": {
"State": "Enabled",
"Health": "OK"
},
"Identifiers": [
{
"DurableNameFormat": "NQN",
"DurableName": "nqn.2014-08.org.nvmexpress:uuid:6c5fe566-10e6-4fb6-aad4-8b4159029384"
}
],
"Capacity": {
"Data": {
"ConsumedBytes": 0,
"AllocatedBytes": 10737418240
}
},
"NVMeNamespaceProperties": {
"NamespaceId": "0x011",
"NamespaceFeatures": {
"SupportsThinProvisioning": false,
"SupportsAtomicTransactionSize": false,
"SupportsDeallocatedOrUnwrittenLBError": false,
"SupportsNGUIDReuse": false,
"

## Slide 15: Redfish Representation of a Composable Disaggregated Infrastructure Redfish Representation of NVMe

## Slide 16: Composable Disaggregated Infrastructure (CDI) in an HPC Architecture Composable Disaggregated HPC system controlled by the OFMF

## Slide 17: OFMF Architecture HardWare Fabric Agents interacting with the OFMF

## Slide 18: OFMF Architecture---The OFMF components

## Slide 19: OFMF Architecture Composable Infrastructure interacting with the OFMF

## Slide 20: Examples of CDI HPC Use-Cases Composable Filesystem on a composable Disaggregated Infrastructure

## Slide 21: Container/Workload Manager Container Composition
Administration Domain
Workload Manager
Container Deployment
Application Domain
Storage
Manager (OpenFam using libFabric)
Container Engine
FAM
Manager (OpenFam using libFabric)
Accelerator
Manager (OpenFam using libFabric)
Batch Job
Interactive Job
Monitoring
Application
OpenFam
LibFabric
OFM Services
Resource Inventory
RESTful API (RF/SF)
Data Store
RF tree management
Authentication
Access Control
Events & Logs
Resource Configuration
Fabric Configuration
Composability Layer
Fabric Resources
Monitoring
Composition
Policies
Resource
Control
(e.g., Compute, FAM, Storage, Fabric)
Data Store
Events & Logs
Message Queue

## Slide 22: Examples of CDI HPC Use-Cases Container Engine interacting with the OFMF

## Slide 23: Example of NVMeoF over and RDMA fabric

## Slide 24: What’s Next for OFMF Development
We are adding Events as a way to provide notifications of changes to the HPC systems
  Events happen when a Hardware Agent provides details about network fabrics that are detected, hardware changes, etc. The events get propagated to the OFMF and to clients.
Redfish Mock-ups for CXL, GenZ, RDMA, Slingshot
OFMF Redfish Tree clean-up and Stranded Resource notifications
Further development of the Reference Fabric Agent framework
Reference Composabilty Manager framework
Reference Fabric Attached Memory framework
Reference Monitoring framework
OS SUPPORT FOR DYNAMIC ADDITION AND DELETION OF RESOURCES
Fish name–Sunfish?
Evangelization of the OFMF to the industry

## Slide 25: Questions?