## Slide 1: Suggestion to Restrict OFMF FAM MemoryDomains to Homogenous Memory
Implicit Requirement on how Agents create the Redfish MemoryDomains that get attached to memory-presenting Endpoints

## Slide 2: Fabric Memory Model – Resource Manager Viewpoint -- Heterogeneous MemoryDomains Are a Problem
Service
Root
Fabrics
CXL
Endpoints
T3
Chassis
PCXL3
Memory Chunks
1
Fabric Adapters
1
Memory Domains
1
Memory
src1
Singleton resource
Collection resource
Subordinate relationship
Associate relationship
ports
2
1
Notes: First there is an endpoint
Redfish schema declares endpoints provide some source or sink entity a logical presence on the fabric. Redfish declares FAM resources are tied to the fabric by a physical entity called a Fabric Adapter
Fabric Adapters have the ports on the physical fabric, providing the Endpoint with physical access
Fabric Adapters that provide access to FAM declare links to one or more MemoryDomains
MemoryDomains are declared to be the memory pools presented to the fabric.
MemoryDomains are funded by physical resources, IE Memory ‘devices’.
  Originally, memory devices were homogeneous things, and one MemoryDomain could be sourced by one or more (whole) Memory devices
  The type, size, and number of memory devices determined the MemoryDomain’s properties and its capacity.
  If the linked source devices are not homogeneous, the MemoryDomain is heterogeneous.
A MemoryChunk derived from a heterogeneous MemoryDomain is harder to define to be a homogeneous chunk. More details about the individual source(s) behind the MemoryDomain are needed.
MemoryChunks were created to model homogeneous ‘pieces’ of memory. Individual MemoryChunks have to be tied back to specific homogeneous Memory sources. (Either a homogeneous subset of a Memory source, or a specific homogeneous Memory source. Redfish does not yet have a schema for linking to a subset of a Memory source, even though heterogeneous Memory objects are currently defined.)
IF the MemoryDomain is not homogeneous, carving off proper (homogeneous) MemoryChunks becomes very difficult for the Resource Manager to do in a hardware agnostic manner. The Resource Manager has to track down the hardware specific details about the Memory sources.

## Slide 3: Fabric Memory Model – Heterogeneous Sources Mapped to Homogeneous MemoryDomains
Service
Root
Fabrics
CXL
Endpoints
T3
Chassis
PCXL3
Memory Chunks
1
Fabric Adapters
1
Memory Domains
1
Memory
src1
Singleton resource
Collection resource
Subordinate relationship
Associate relationship
ports
2
1
2
src 1
src 2
Notes: First there is an endpoint
Redfish schema declares endpoints provide some source or sink entity a logical presence on the fabric. Redfish declares FAM resources are tied to the fabric by a physical entity called a Fabric Adapter
Fabric Adapters have the ports on the physical fabric, providing the Endpoint with physical access
Fabric Adapters that provide access to FAM declare links to one or more MemoryDomains
MemoryDomains are declared to be the memory pools presented to the fabric.
MemoryDomains are funded by physical resources, IE Memory ‘devices’.
  Originally, memory devices were homogeneous things, and one MemoryDomain could be sourced by one or more (whole) Memory devices
  The type, size, and number of memory devices determined the MemoryDomain’s properties and its capacity.
One Memory device could be totally consumed by one MemoryDomain
A MemoryDomain that was sourced by one Memory device was homogeneous, just like its source.
A homogeneous MemoryDomain makes an easy object to model a ‘homogeneous memory pool’ from which to carve out homogeneous Memory Chunks.
And now the Resource managers do not have to understand the hardware Memory sources behind the MemoryDomains (unless they want to)
  No details are lost, but the RMs can be generic and stick to processing Memory Pools, Memory Chunks, and Logical Memory Regions at an abstract level.
The OFMF requirement of homogeneous MemoryDomains can be met by the Agent/FM stack in a couple of ways. The method shown requires enhancements to Redfish MemoryDomain allowed links.
An easier mechanism might be to breakdown heterogeneous Memory sources into homogeneous sources, which changes the interpretation of the Memory Collection instances (no longer a complete device), but does not necessarily require Redfish Schema changes.
Remember, the Agent/FM stack chooses how to model the physical resources in a set of Redfish objects.
The rest is just setting policies for Agents/FMs to follow that define WHAT a Memory ‘source’ means, WHAT a MemoryDomain means, and WHAT a Memory Chunk means, so that Clients can have these simpler definitions to work with when doing ‘discovery’ on the Redfish Service tree. There are obviously other ways to make it easier to carve homogeneous MemoryChunks out of more heterogeneous MemoryDomains. OFMF should recommend a policy and preferred implementation and proceed with the reference implementation.

## Slide 4: Text Summary for the FAM problem
MemoryChunks are the finest-grained FAM resources which are modeled by Redfish.
FMs and Redfish Services need a global handle to share MemoryChunks among multiple Hosts
  Redfish URI is not globally unique, just Redfish Service unique
  Redfish MemoryChunk objects should have a UUID to support this need
FMs need a fabric-specific and fabric-unique handle to manage these MemoryChunks on the fabric HW
MemoryChunks cannot cross hardware-mandated boundaries (eg. media type, decoder boundaries)
MemoryChunks cannot cross software-mandated boundaries (eg. Media type, permission domains)
Memorychunks are therefore ‘homogeneous’ wrt these restrictions
MemoryChunks are subordinates of MemoryDomains; they cannot cross over between MemoryDomains
At the same time, Clients of the Redfish Services have expectations about MemoryDomains and MemoryChunks none of which are written down yet. A few, key expectations Sunfish should anticipate:
MemoryChunks are homogeneous wrt persistence, general NUMA domains, permissions
Persistent Memory pools and Volatile Memory pools may need different Resource Managers
Different managers of different pools should not have access to Redfish access to other pools
  Otherwise Control permissions must be by MemoryChunk rather than by MemoryDomain
Allowing a single MemoryDomain to model heterogeneous Memory sources makes it much harder to hide hybrid memory devices from the Redfish Service Clients and provide isolation between pool managers.
The recommendation is that Sunfish present only ‘homogeneous’ MemoryDomains in the Redfish models for Fabric Attached Memory (FAM)

## Slide 5: Bottom Line Recommendation
There are obviously other ways to make it easier to carve homogeneous MemoryChunks out of more heterogeneous MemoryDomains, but the OFMF charter is to offer the ‘Easy Button’.
OFMF needs to recommend a policy and proceed with the reference implementation.
Recommendation:
Accept that Memory Collection instances that fund FAM pools behind a Fabric Adapter are not required to be precise models of specific memory devices.
Model FAM sources as aggregations of generic DRAM based Memory sources (for volatile capacity) and aggregations of some form of ‘Persistent’ Memory sources
Create homogeneous MemoryDomains from the appropriate collection of homogeneous Memory sources.
Place more fabric and vendor specific details about Memory sources in fabric specific and vendor OEM fields, in case fabric-aware Clients need or want these details.
The above is believed possible without defining new schema for Redfish. This assumption needs to be validated.
This recommendation does not prohibit alternative methods to create homogeneous MemoryDomains

## Slide 6: Accompanying Rules for FM’s and Agents
When creating a Redfish MemoryDomain to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
InterleavableMemorySets The interleave sets for the memory chunk. Array of sets of interleaved sources which fund this MemoryDomain.
MemorySet The set of memory for a particular interleave set. The array of URI’s pointing to memory resources for a particular interleave set
Unfortunately, there is no mechanism (yet) to point to a subset of a memory resource. Also, no way to do without these links.
@odata.id Link to a Memory resource
Apparently assumed to be a homogeneous Memory ‘device’?
Must be present to enable clients to determine Memory properties.
MemorySizeMiB : The total size of the memory domain in mebibytes (MiB)
Assumed to be the summation of all capacity of all Memory resources linked in the InterleavableMemorySets. Unfortunately, there is no way to tell if all this capacity is homogeneous, or of what basic properties (volatile, non-volatile, other)
Otherwise, This value might as well be ignored by a Sunfish (OFMF) client.
NOTE: Because almost no details about the actual memory media are included in the MemoryDomain description (as of Version 2023.1WIP99), the InterleavableMemorySets details must be present and must tie the MemoryDomain to one or more Memory instances.
Red: changes proposed in wording Green: comments for discussion

## Slide 7: Accompanying Rules for FM’s and Agents
When creating a Redfish Memory resource (not a Memory device) (Memory instance) to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
The Memory schema represents a memory device, such as a DIMM, and its configuration., or a generic set of media sources that are presented to a memory semantic fabric by a Fabric Adapter object.
The original definition of a Redfish Memory instance was very ‘memory device’ centric. FAM resources located behind a Fabric Adapter may be presented as generic pools of volatile or non-volatile byte addressable storage. In some cases, there are few details about the physical memory devices to be made known to the outside world.
MemoryType: use DRAM for generic volatile capacity. Use NVDIMM_F for generic persistent capacity. If the physical memory device is hybrid (such as IntelOptane, or NVDIMM_N or NVDIMM_P), the Memory instance shall use the Regions property to describe homogeneous Regions)
Regions:
MemoryClassification: use ByteAccessiblePersistence for persistent ranges, and use Volatile for the non-persistent ranges
NOTE: Currently (Version: 2023.1WIP99) there is no way to link a MemoryDomain to a Regions object within a Memory object. Until that situation is corrected, if the FM/Agent stack wishes to model FAM using homogeneous MemoryDomains, the FM/Agent stack should arbitrarily model the Memory Instances as generic, homogeneous Memory objects in the Memory collections.
Red: changes proposed in wording Green: comments for discussion

## Slide 8: Accompanying Rules for FM’s and Agents
When creating a Redfish Memory resource (not a Memory device) (Memory instance) to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
Truly hybrid memory devices can be modeled as two or more Memory instances (sources) with the appropriate homogeneous properties segregated into different Memory instances. The common details shall be identical in each Memory instance.
CapacityMiB: total capacity of this Memory instance’s included Regions
‘Device’ level properties that are specific to a Region-specific property (such as persistence) are only present in the Memory instance containing the related Regions description.
PersistentRegion*: only included in Memory instances containing Regions with persistent capacity
Volatile*: only included in Memory instances containing Regions with volatile capacity
Each homogeneous Memory instance shall include a Regions array containing Regions objects that describe the appropriate homogeneous Regions of the hybrid memory device.
Regions
RegionID: shall be unique across all Memory instances used to describe the total hybrid device capacity
SizeMiB: shall be the size of this Region, as always
OffsetMiB: shall be the starting offset of this Region from the base that would be used in a complete hybrid device model, but this is not an offset that has meaning outside the Redfish address space defined by the FM/Agent stack that creates the Memory resource object. This offset has no meaning to individual Hosts on the CXL fabric! See MemoryChunk discussion
Red: changes proposed in wording Green: comments for discussion

## Slide 9: Accompanying Rules for FM’s and Agents
When creating a Redfish MemoryDomain to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
MemorySizeMiB : The total size of the memory domain in mebibytes (MiB)
Assumed to be the summation of all capacity of all Memory resources linked in the InterleavableMemorySets, but only IF HOMOGENEOUS.
A possible working restriction for Sunfish:
If MemorySizeMiB is not present, the MemoryDomain cannot be assumed to be homogeneous, and the Client shall trace the Memory resources themselves to create the client’s view of one or more memory pools available from this MemoryDomain.
  If MemorySizeMiB is present, the MemoryDomain shall be homogeneous, and if the Client wishes to know more details, it may trace the Memory resources. If not, the Client can do allocations of MemoryChunks from this MemoryDomain as it sees fit.
  NOTE: there is still no MemoryDomain memory type (persistent, volatile, mixed) property. Currently, a client must still trace at least one memory source to learn the basic properties of the domain.
Red: changes proposed in wording
Green: comments for discussion

## Slide 10: Accompanying Rules for FM’s and Agents
When creating a Redfish MemoryChunk to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
AddressRangeOffsetMiB : Offset of the memory chunk in the MemoryDomain address range in MiB
Assumes the Offset is from start of MemoryDomain. If the MemoryDomain is not Homogeneous, then this offset is ambiguous.
If the MemoryDomain is Homogeneous, this offset makes sense only within the Redfish context.
Unfortunately, the CXL context has potentially different ‘address spaces’ for each host, and there is No single address space for the entire CXL fabric.
The Gen-Z FM/Agent stack owned the single ‘memory pool address’ of the whole Gen-Z device, and provided a MemoryDomain with a linear memory pool address from 0 to size-1 bytes. There was no additional translation between the AddressRangeOffsetMiB value assigned by the ResourceManager and where the Gen-Z device placed the start of the MemoryChunk.
However, CXL has no single ‘memory pool address’ visible to the FM. So there is no known correlation between what the Resource Manager (who creates a Chunk from a Domain) calls the starting address, and what the CXL memory controller will call the starting address. Further, each Host may be given its own ‘Device Physical Address’ space by the CXL device.
Thus, what Redfish tracks as the AddressRangeOffsetMiB is not guaranteed to be what the CXL device informs the Host to use as the starting address in the Host’s DPA space!
Red: changes proposed in wording Green: comments for discussion