## Slide 1: Enumerating Requirements for Redfish FAM modelling
Example Requirements on how Agents create the Redfish models of CXL Multiple Logical Devices and how specific properties of the resulting objects are to be interpreted
Russ Herrell / John Mayfield HPE
5/26/23

## Slide 2: Disclaimer
The tables of rules herein were developed at a different snapshot in time from the animated bubble diagrams.
There are no guarantees that these text examples are completely consistent with the bubble diagrams.
The bubble diagrams are newer and therefore likely more accurate, but nothing herein is anything more than a draft.
All content is proposed to the OFA’s OpenFabrics Management Framework Work Group as representative of content to be included in the OFMF’s Architecture documentation.
None of the content is intended to imply changes to Redfish definitions and schema; we are attempting to establish Sunfish interpretations of and restrictions on Redfish modelling of certain fabric resources.

## Slide 3: Fabric Memory Model – Heterogeneous Sources Mapped to Homogeneous MemoryDomains
Service
Root
Fabrics
CXL
Endpoints
T3
Chassis
PCXL3
Memory Chunks
1
Fabric Adapters
1
Memory Domains
1
Memory
Singleton resource
Collection resource
Subordinate relationship
Associate relationship
ports
2
1
2
src 1
src 2
Notes: First there is an endpoint that can be the source or sink of packets on the fabric. Endpoints can be physical or logical.
Redfish declares FAM resources are tied to the fabric by a physical entity called a Fabric Adapter.
Fabric Adapters have the ports on the physical fabric, providing the Endpoint with physical access
MemoryDomains are funded by physical resources, IE Memory ‘devices’, ‘sources’, or ‘resources’.
  Originally, memory devices were homogeneous things, and one MemoryDomain could be sourced by one or more (whole) Memory devices
  The type, size, and number of memory devices determined the MemoryDomain’s properties and its capacity.
Fabric Adapters that provide access to FAM declare links to one or more MemoryDomains
MemoryDomains are declared to be the memory pools presented to the fabric.
If the source or sources of Memory are not homogeneous, the FM/Agent needs to segregate al capacity into some number of homogeneous Memory sources that fund homogeneous MemoryDomains.
A homogeneous MemoryDomain makes an easy object to model a ‘homogeneous memory pool’ from which to carve out homogeneous Memory Chunks.
And now the Resource managers do not have to understand the hardware Memory sources behind the MemoryDomains (unless they want to)
  No details are lost, but the RMs can be generic and stick to processing Memory Pools, Memory Chunks, and Logical Memory Regions at an abstract level.
The OFMF requirement of homogeneous MemoryDomains can be met by the Agent/FM stack in a couple of ways. The method shown requires the FM to sort the FAM sources behind the FabricAdapter into homogeneous Memory ‘resources’ so the Redfish Service Clients do not have to.
The rest is just setting policies for Agents/FMs to follow that define WHAT a Memory ‘source’ means, WHAT a MemoryDomain means, and WHAT a Memory Chunk means, so that Clients can have these simpler definitions to work with when doing ‘discovery’ on the Redfish Service tree. There are obviously other ways to make it easier to carve homogeneous MemoryChunks out of more heterogeneous MemoryDomains. OFMF should recommend a policy and preferred implementation and proceed with the reference implementation.

## Slide 4: Fabric Memory Model – MLDs and Logical Devices
Service
Root
Fabrics
CXL
Endpoints
T3
Chassis
PCXL3
Memory Chunks
1
Fabric Adapters
1
Memory Domains
1
Memory
Singleton resource
Collection resource
Subordinate relationship
Associate relationship
ports
2
1
2
src 1
src 2
PCIe Devices
1
PCIe Functions
1
CXL Logical Devices
1
T4
Notes:   Now let’s look at how to model a multi-logical-device presented by the MLD.
  Because the MLD is a FAM provider to the fabric, the FM will discover it and model it initially as a FAM device
  Then, because the MLD provides its FAM capacity through one or more CXL Logical Devices, the FM can pre-populate the LDs into the Redfish Fabric Service tree.
The FM pre-populates the expected PCIe structures which host the MLD’s Logical Devices. The FM may not know all the PCIe specific mapping details (for example Bus/Device/Function numbers, PCIe bus width, etc), but the CXL Logical Device is dictated to be placed in this default location in the Redfish tree for a FAM device.
For interoperability, we propose that a CXL Logical Device be mapped to its own (logical) Endpoint object on the fabric.
Before any specific memory resources are allocated to this Logic Device, the FM must tie it to the FabricAdapter that sources it to the fabric. This shall be done by tying its Endpoint back to the FabricAdapters port
Another method to link ‘place holder CXL Logical Devices’ to their sourcing entity shall be to create a link from the LD to its PCIe device (physical device).
This is as far as the FM can go in completing the model without a plan that creates MemoryChunks and binds them to specific Logical Devices.
Certainly, an SLD or even the LD’s of an MLD may contain some memory pre-allocated to a given Logical Device.
For pre-allocated memory the FM/Agent modeling the FAM resources will create a MemoryChunk out of some of the capacity of our FAM device. Pre-allocated memory resources that are not dynamically migrated shall have their own MemoryDomain / Memory source. Basically pre-allocated memory and dynamically allocated memory shall not be modelled in the same MemoryDomain..
Pre-allocated memory shall be modelled as one or more MemoryChunks already linked to LD 1 of the MLD. This binding may create many cross linkages, but the important ones are the Endpoint to Chunk, the LogicalDevice to Chunk, and the LogicalDevice to parent MemoryDomain.
At this point there is no host tied to the LD.

## Slide 5: Fabric Memory Model – MLDs and Logical Devices
Service
Root
Fabrics
CXL
Endpoints
T3
Chassis
PCXL3
Memory Chunks
1
Fabric Adapters
1
Memory Domains
1
Memory
Singleton resource
Collection resource
Subordinate relationship
Associate relationship
ports
2
1
2
src 1
src 2
PCIe Devices
1
PCIe Functions
1
CXL Logical Devices
1
T4
3
src 3
Memory Chunks
1
2
T5
Notes: Starting with a model that could have been an SLD as easily as it was an MLD, let’s add a second LD in the example.
The FM would find ALL the potential Logical Devices available on the MLD (FabricAdapter), we’ll show just a second LD. The FM will find the memory source for pre-allocated capacity for each LD, model the Memory source and the associated MemoryDomain
Like before, the capacity pre-allocated to an LD is modelled as a pre-allocated MemoryChunk and linked to the LD
The FM shall then create the new logical Endpoint and link it into the physical FabricAdapter Port, the Logical Device (as the ConnectedEntity) and link in the pre-allocated MemoryChunk(s)
At this point there is still no host tied to the LD.
However, a Client can now walk the Endpoint Collection of the CXL fabric and discover the FAM physical device, all its pre-allocated and free memory pools, the Logical Devices and their pre-allocated memory capacities.
Not shown: The optional Dynamic Capacity structures that an MLD might also contain.

## Slide 6: Accompanying Rules for FM’s and Agents
When creating a Redfish FabricAdapter to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
Property | Type | Client / FM | Notes
FabricType | string | FM crawlout | The configured fabric type of this fabric adapter. Some NICs support multiple protocols. This property shall declare the FabricType currently configured. If the adapter is re-configured, this Redfish instance shall be deleted and a new one created.
Links/Endpoints | array | FM crawlout | Links to all Endpoint objects presented to the fabric by this adapter. See the Sunfish definition of Endpoint.
Links/MemoryDomains | array | FM crawlout | Links to homogeneous MemoryDomain objects which are to be used as memory pools sourced by this FabricAdapter
Ports | array | FM crawlout | Link to the subordinate collection of Port objects that exist on the FabricAdapter
UUID | string | FM crawlout | A UUID-formatted string that uniquely identifies this FabricAdapter instance within the scope of the Fabric or Fabrics on which this adapter represents an Endpoint.
Examples DRAFT
Notes: These tables of rules were developed as a different snapshot in time from the animated bubble diagrams.
There are no guarantees that these examples are completely consistent with the bubble diagrams.
The bubble diagrams are newer and therefore likely more accurate, but nothing herein is anything more than a draft.

## Slide 7: Accompanying Rules for FM’s and Agents
When creating a Redfish MemoryDomain to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties:
Property | Type | Client / FM | Notes
InterleavableMemorySets/MemorySet | array | FM crawlout | Links to all Memory resource objects that fund this MemoryDomain. All such Memory resources shall be homogeneous.
Links/FabricAdapters | array | FM crawlout | Array of Links to all FabricAdapters that may present MemoryDomain resources to the fabric. Typically, an array of one link, but not mandated to be.
Links/CXLLogicalDevices | array | Client binding | Array of links to all CXLLogicalDevices presenting portions of this MemoryDomain as resources of the Logical Device.
MemoryChunks | link | FM crawlout | Link to the subordinate collection of MemoryChunk objects that are funded by this MemoryDomain
MemorySizeMiB | int | FM crawlout | Total size of the homogeneous MemoryDomain. If present, shall represent available capacity of all sources in the homogeneous InterleavableMemorySets. Shall not be present if the InterleavableMemorySets are not homogeneous.
Examples DRAFT

## Slide 8: Accompanying Rules for FM’s and Agents
When creating a Redfish MemoryChunk to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties: (1 of 2)
Property | Type | Client / FM | Notes
DisplayName | String | Client create | 16-character (16-byte) UUID formatted string assigned by the chunk creator. DisplayName is unique across the Fabric or Fabrics to which the MemoryChunk instance is connected through an associated FabricAdapter.
AddressRangeType | String | FM crawlout | Basic memory type (Block, PMEM, Volatile) of entire chunk. This property is dictated by the properties of the Memory sources making up the MemoryDomain from which this chunk is allocated.
AddressRangeOffsetMiB | Int | Client/FM | Offset of the MemoryChunk in MiB from base (0) of the MemoryDomain as set by the creator of the chunk. This offset may or may not be meaningful to the FM or the actual device.
MediaLocation | String | Client create | For MemoryChunk instances of FAM, this value shall always be set to “Local”. (Options are Local, Mixed, Remote) When modeling FAM MemoryChunks for Sunfish, such chunks shall only be allocated from Memory sources assumed to be co-located within a single MemoryDomain, and thus ‘local’ to the associated FabricAdapter(s). Sunfish shall use the Redfish Logical Memory Region (WIP) to model aggregation of multiple MemoryChunks into larger FAM memory pools.
Examples DRAFT

## Slide 9: Accompanying Rules for FM’s and Agents
When creating a Redfish MemoryChunk to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties: (2 of 2)
Property | Type | Client / FM | Notes
Links/Endpoints | Array | Client create | Array of links to Endpoint objects that make this MemoryChunk accessible from the Fabric(s).
Links/CXLLogicalDevices | Array | Client create | Array of links to any CXLLogicalDevices that use this MemoryChunk to fund Logical Device capacity
InterleaveSets/ Memory/ OffsetMiB RegionID SizeMiB | Array | FM create | Optional For MemoryChunk instances of FAM, Since FAM MemoryChunks are created from Memory resources ‘local’ to the FabricAdapter the Client may not have the ability to specify the exact Memory resources that will fund a MemoryChunk. The FM/Agent stack may return these details if it can extract them from the hardware. A Sunfish FAM MemoryChunk shall only be allocated from a single RegionID of a multi-region Memory source. This prevents need for multiple passphrases associated with a single MemoryChunk.
Examples DRAFT

## Slide 10: Accompanying Rules for FM’s and Agents
When creating a Redfish homogeneous Memory resource to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties: (1 of 2)
Property | Type | Client / FM | Notes
CapacityMiB | Int | FM crawlout | Memory capacity in MiB. This Property shall only be present if all capacity in the resource object is homogeneous. (The FM/Agent stack shall model all FAM Memory resource instances as homogeneous sources.)
OperatingMemoryModes | Array | FM crawlout | Array of strings describing the memory modes supported by this Memory resource. (Block, PMEM, Volatile) If more than one mode is listed in the array, this is NOT a homogeneous Memory resource.
Regions | Array | FM crawlout | Array of Region descriptions that define homogeneous sub-ranges of memory capacity within this Memory resource
Examples DRAFT

## Slide 11: Accompanying Rules for FM’s and Agents
When creating a Redfish homogeneous Memory resource to describe FAM, the FM/Agent stack shall use the following interpretations for specific Properties: (2 of 2)
Property | Type | Client / FM | Notes
Regions/ MemoryClassification | String | FM crawlout | Basic memory type (Block, PMEM, Volatile) of entire region. This property dictates the corresponding AddressRangeType property of the MemoryDomain funded by this Region. A homogeneous Sunfish FAM Memory resource shall have the same MemoryClassification in all Regions
Regions/RegionID | String | FM crawlout | Unique region ID associated with this Region. Unique value across all associated Memory resources used to model the memory capacity of a non-homogeneous memory source associated with a FAM FabricAdapter.
Regions/SizeMiB | Int | FM crawlout | Size of this Region in MiB.
Regions/OffsetMiB | Int | FM crawlout | Offset of the Region in MiB from base (0) of the Memory resource. (Optional) Some fabrics do not make such an offset visible outside the memory device. This offset, if present, may or may not be meaningful to the Sunfish client, the FM or the actual device.
Examples DRAFT