## Slide 1: Sunfish
SC24 Sunfish Birds of a Feather
SAND2024-15345C

## Slide 2: Sunfish
Overview and Introduction of Sunfish (Michael Aguilar, Sandia)
H3 Presentation of CXL Sunfish Agents (Brian Pan, H3)
Flux/Sunfish (Nathan Hanford, LLNL)
Discussion
Notes: Welcome to the Sunfish BoF session. My name is Michael Aguilar and I am a Co-Chair for the OpenFabrics Management Framework Working Group. I will be providing you with a quick overview of Sunfish and then I will be introducing Brian Pan of H3 Platform who will be demonstrating their implementationof NVMe over CXL using Sunfish to manage compute node aggregation. Nathan Hanford will be discussing the integration of Sunfish with Flux to provide direct HPC resource allocation.

## Slide 3: Composable disaggregated resources
Composable Disaggregated Resources:
    Can potentially reduce capital expenditures and operating expenses
    Feed the beast’ in terms of workload (e.g., AI, HPC) data requirements
Composable Disaggregated Infrastructure (CDI)
    Computational resources are physically separated over high-speed/low-latency fabrics
    Computational resources are dynamically composable, as needed, into a computer system
Composable HPC and Enterprise Computing Systems:
    Enable efficient usage of available hardware resources by provisioning it where it is needed
    Mitigate the need for hardware overprovisioning
    Reduce electricity consumption and cooling costs
      4% of the World’s Energy Consumption is input into Datacenters
      (https://www.energy.gov/eere/buildings/data-centers-and-servers)
Notes: Current HPCs are designed to provide node allocation, not resource allocation. For fully populated compute nodes, this can lead to ‘resource stranding’, or unused resources within the HPC system. In the current approach, you are still paying for energy and cooling. In fact, a vendor that I met with was proposing measuring the amount of unused resources in each batch run, as part of their new tooling. A better approach would be to be able to allocate resources from resource pools to each batch job running on the cluster.

## Slide 4: Management of disaggregated resources
GPU
NVMe
HCA
GPU
FPGA
NVMe
DRAM
DRAM
CPU
DRAM
Sunfish Services
Resource Inventory
Redfish Tree
RF tree management
Authentication
Access Control
Events & Logs
Resource Configuration
Fabric Configuration
Notes: In an HPC, at scale, there are a very large quantity of resources and it’s necessary to be able to ‘wrangle’ them. That’s why we are creating Sunfish. Sunfish is a framework that provides both Redfish, as a central database, and tools.

## Slide 5: Sunfish
Comprehend dynamic hardware resources – event driven updating of available resources
Dynamically reserve resources and release allocated resources
Sunfish Services
Resource Inventory
Hardware Layer
CXL
Agent
Redfish Tree
RedFish
Vendor Native API
RF tree management
Authentication
Access Control
Events & Logs
Resource Configuration
Fabric Configuration
CXL Manager
SAN
Agent
Fabric Manager
Appliance Manager
Management Layer

## Slide 6: Sunfish
Sunfish enables optimized resource/workload placement
Sunfish Services
Resource Inventory
RESTful API (RF/SF)
Redfish Tree
RF tree management
Authentication
Access Control
Events & Logs
Resource Configuration
Fabric Configuration
Resource Control Operations
(e.g., Compute, FAM, Storage Fabric)
Resource Events
Composition Policies
Resource Graph Representation
(e.g., Compute, FAM, Storage Fabric
Graph Reference Database
Graph Reference Database
Authorization Block
Graph Reference Database Entry
Events
Transactions
Data
Evaluate Client Requirements
Redfish/Swordfish
Message Queue
The Sunfish Composability Manager provides Application Domain Clients with Deep-Learning Resource Aggregation Optimization, a Graph Database for informational queries, and can reduce the amount of traffic to the Sunfish Core services.

## Slide 7: H3 Platforms/Sunfish Presentation
Brian Pan from H3 Platform

## Slide 8: Flux/Sunfish Presentation
8
Clients
Management Layer
CDI Composition Interface
Redfish/Swordfish
Graph Reference Database
Resource Control Operations
Resource Graph Representation
Resource Events
Evaluate Client Requirements
Composition Policies
Authorization Block
DB Entry
Sunfish Services
Message Queue
RESTful API (RF/SF)
Events
Data
Transactions
Resource Inventory
RF Tree Management
Resource Configuration
Fabric Configuration
Authentication
Access Control
Events and Logs
Redfish Tree
Virtual Cluster Managers
Flux
API
Integration
Module
Nathan Hanford from Lawrence-Livermore National Lab

## Slide 9: Sunfish status, next steps, and discussion
Soliciting new use cases and hardware
  Started working on the Flux client side integration
  New endpoint models
  New workflows
Exploring reference architecture for client-side resource managers
Developing a reference CXL Agent and associated utilities
Integrating SNIA Swordfish as an NVMe technology Agent
Architecting customization plugin and Redis storage backend
Finalizing documentation for Sunfish version 0.6