# IBDM

IBNL

# A Generic IB Netlist Format

Revisions Table:

| Revision | Date | Updated By | Modification High Level |
| --- | --- | --- | --- |
| 1.0 | 29/9/2004 | Eitan Zahavi | Initial revision |
| 1.1 | 5/7/2005 | Eitan Zahavi | Remove IBADM from the definition. Real effect only on target dir for the package: $prefix/lib/ibdm1.0 |

# Overview

IBDM topology file provide means to describe the IB fabric using a set of predefined systems. A system definition is provided in a single file in IBNL format that describes the internal InfiniBand connectivity of the system in terms of boards and devices. When IBDM starts it parses all the available system definition files before it handles the topology file. The files are located in the following directory relative to the installation prefix: <prefix>/lib/ ibdm1.0/ibnl. Any new system that is described using the IBNL file format and has a corresponding file in this directory is supported by IBDM.

This appendix describes the IBNL file format used to define an arbitrary IB system internal IB connectivity. It outlines the main concepts used by the file, provides details for how to obtain such a file, a formal definition of the file syntax in BNF like format (YACC/Bison readable) and concludes with real life example.

## Main Concepts:

The described file format for defining generic system IB connectivity uses the following terminology:

NODE – The instantiation of an IB device may it be a switch or a channel adapter.

SUB-SYSTEM – The instantiation of a board or module in a system.

SYSTEM – A definition of a board or a module.

TOPSYSTEM – The top most system defined in the given file.

SUB-SYSTEM MODIFIER – Many systems allow multiple variations of their sub-system such as a 12X version of a leaf board in a MTS9600. The modifier is a suffix to the board name and should follow the format “: <any name>”. The IBNL format supports assigning multiple names to the same board.

## File Format:

The IBNL file is line sensitive as it requires different sections to start on a new line. The file is broken into several SYSTEM (optional) and one TOPSYSTEM sections. Each has one or more names. The following diagram describes the file in more details:

Figure 1 - IBNL File Sections

Connections are defined inside the system level only and thus might be of two types:

- Between any node or sub-system to other node or sub-system

- From any node or sub-system to a connector of the system.

Note: The top system can define ports that might be redundant and not connected to any lower level board connector. In these cases the ports are simply omitted from the resulting system. This feature enables defining the front panel ports of a 12X/4X such that if a 12X leaf is selected only the 12X front panel ports are used.

Another important note is that port width and speed provided at the lowest level have precedence over definitions provided at upper levels of the hierarchy.

## Writing a System IBNL File

The following procedure should be followed in order to provide a new system IBNL:

- Name the file after the system name: <any sys name (no spaces)>.ibl

- Define a SYSTEM section for each board included in the system

- The port names of the boards are just strings, we use the simple format of P<N> where N is just a serial number but you can pick any name you want. Just make sure it is unique.

- When different flavors of the boards exists – like when you have a 4x and 12x option for a board – name the optional boards with a “modifier postfix”. An example for such system that supports a LEAF board of 12x and 4x types would be to define two SYSTEMS:

SYSTEM LEAF,LEAF:4x,LEAF:4X

…

SYSTEM LEAF:12x,LEAF:12X

…

Note that the instantiations of the LEAF boards in another board or the top system need not specify the postfix and are being decided upon only when the topology file is being parsed. The “SYSTEM LEAF” with no postfix will be used by default. To continue the example here is how the LEAFs are instantiated in the top system:

TOPSYSTEM MyIbSystem

LEAF leaf1

…

LEAF leaf2

…

The actual 4x or 12x version of the LEAF board can then be specified in the topology file CFG section to select the right combination of optional boards in the system. An example will be:

MyIbSystem N001 CFG: leaf2=12x

In this case leaf1 will be 4x as no special modifier is defined for it (and LEAF is by default a 4x leaf). Leaf2 will eb 12x as defined in the CFG section,

- Special considerations should be made to design the top system section when several optional board types exist. Top system section might include multiple definitions for front panel plugs like P1-4x and P1-12x (yes these are just names that should follow the writing on the front or back panels). As the different flavors of the boards are not required to define the same names for their ports – including a 12x port might leave some of the top level connections dangling (not connected) and thus the front panel ports of the other flavor will be removed from the final system definition.

As an example let us consider a simple board LEAF with 3 4x port flavor and one 12x port flavors. We recommend connecting it in the top level using the following scheme:

SYSTEM LEAF:4x

NODE … U1

1 -4x-> 4XP1

2 -4x-> 4XP2

3 -4x-> 4XP3

…..

SYSTEM LEAF:12x

NODE … U1

1 -12x-> 12XP1

…..

TOPSYSTEM myIbSystem

SUBSYSTEM LEAF leaf1

4XP1 -> L1/P1

4XP2 -> L1/P2

4XP3 -> L1/P3

12XP1 -> L1/P1-12x

- Place the file in the <prefix>/lib/IBDM/ibdm1.0/ibnl directory

- To check the file syntax you have two options:

  - Using the ibnlparse utility:

Usage: ibnlparse <ib netlist file> <sys type>

Where the system type is the top system name.

  - By parsing it in context of a topology file using the utility ibdmtr (trace a direct route through the fabric):

    - Define a topology file with your new system

    - Set some CFG options if applicable

    - Invoke: ibdmtr -t <topo file> -s <any node>/U1  -p 1 –d 0,1

## Formal definition in YACC Syntax:

INT ::= ([1-9][0-9]*|0) ;

WIDTH ::= (4x|8x|12x) ;

SPEED ::= (2.5G|5G|10G) ;

NODETYPE ::= (SW|CA|HCA) ;

NAME ::= ([\[\]\\\*/A-Za-z0-9_.:%@~]+) ;

NL:

LINE

| NL LINE;

ONL:

| NL;

ibnl: ONL systems topsystem;

systems:

| systems system ;

sub_inst_attributes:

| sub_inst_attributes sub_inst_attribute NL;

sub_inst_attribute:

NAME '=' NAME '=' NAME

| NAME '=' NAME '=' INT

| NAME '=' NAME ;

topsystem:

TOPSYSTEM  system_names  NL sub_inst_attributes  insts ;

system:

SYSTEM system_names  NL insts ;

system_names:

system_name

| system_names ',' system_name ;

system_name:

NAME ;

insts:

| insts node

| insts subsystem ;

node:

node_header NL node_connections ;

node_header:

NODE NODETYPE INT NAME NAME ;

node_connections:

| node_connections node_connection NL ;

node_connection:

node_to_node_link

| node_to_port_link ;

node_to_node_link:

INT '-' WIDTH '-' SPEED '-' '>' NAME

| INT '-' WIDTH '-' '>' NAME INT

| INT '-' SPEED '-' '>' NAME INT

| INT '-' '>' NAME INT ;

node_to_port_link:

INT '-' WIDTH '-' SPEED '-' '>' NAME

| INT '-' WIDTH '-' '>' NAME

| INT '-' SPEED '-' '>' NAME

| INT '-' '>' NAME ;

subsystem:

subsystem_header NL subsystem_connections ;

subsystem_header:

SUBSYSTEM NAME NAME ;

subsystem_connections:

| subsystem_connections subsystem_connection NL ;

subsystem_connection:

subsystem_to_subsystem_link

| subsystem_to_port_link ;

subsystem_to_subsystem_link:

NAME '-' WIDTH '-' SPEED '-' '>' NAME NAME

| NAME '-' WIDTH '-' '>' NAME NAME

| NAME '-' SPEED '-' '>' NAME NAME

| NAME '-' '>' NAME NAME ;

subsystem_to_port_link:

NAME '-' WIDTH '-' SPEED '-' '>' NAME

| NAME '-' WIDTH '-' '>' NAME

| NAME '-' SPEED '-' '>' NAME

| NAME '-' '>' NAME ;

## Example IBNL for MTS14400

We provide here a partial (one spine and  2 leafs) IBNL for MTS14400

SYSTEM LEAF,LEAF:4x,LEAF:4X

NODE SW 24 MT47396 U1

1  -> P13

2  -> P14

3  -> P15

4  -> P16

5  -> P17

6  -> P18

7  -> P19

8  -> P20

9  -> P21

10 -> P22

11 -> P23

12 -> P24

13 -> P1

14 -> P2

15 -> P3

16 -> P4

17 -> P5

18 -> P6

19 -> P7

20 -> P8

21 -> P9

22 -> P10

23 -> P11

24 -> P12

SYSTEM LEAF:12x,LEAF:12X

NODE SW 24 MT47396 U1

1  -12x-> P13

4  -12x-> P14

7  -12x-> P15

10 -12x-> P16

13 -> P1

14 -> P2

15 -> P3

16 -> P4

17 -> P5

18 -> P6

19 -> P7

20 -> P8

21 -> P9

22 -> P10

23 -> P11

24 -> P12

SYSTEM SPINE,SPINE:4x,SPINE:4X

NODE SW 24 MT47396 U1

21 -> P63

22 -> P30

23 -> P18

24 -> P6

1 -> P27

2 -> P15

3 -> P3

4 -> P31

5 -> P19

6 -> P7

7 -> P34

8 -> P22

9 -> P10

10 -> P43

11 -> P55

12 -> P67

13 -> P46

14 -> P58

15 -> P70

16 -> P42

17 -> P54

18 -> P66

20 -> P51

19 -> P39

NODE SW 24 MT47396 U2

10 -> P44

11 -> P56

12 -> P68

13 -> P47

14 -> P59

15 -> P71

16 -> P41

17 -> P53

18 -> P65

20 -> P50

19 -> P38

21 -> P62

22 -> P29

23 -> P17

24 -> P5

1 -> P26

2 -> P14

3 -> P2

4 -> P32

5 -> P20

6 -> P8

7 -> P35

8 -> P23

9 -> P11

NODE SW 24 MT47396 U3

9 -> P12

10 -> P45

11 -> P57

12 -> P69

13 -> P48

14 -> P60

15 -> P72

16 -> P40

17 -> P52

18 -> P64

20 -> P49

19 -> P37

21 -> P61

22 -> P28

23 -> P16

24 -> P4

1 -> P25

2 -> P13

3 -> P1

4 -> P33

5 -> P21

6 -> P9

7 -> P36

8 -> P24

TOPSYSTEM MTS14400,Rhino

spine1/U1=isBmaAgent

SUBSYSTEM LEAF leaf1

P1 -> spine1 P1

P2 -> spine1 P2

P3 -> spine1 P3

P4 -> spine1 P4

P5 -> spine1 P5

P6 -> spine1 P6

P7 -> spine2 P7

P8 -> spine2 P8

P9 -> spine2 P9

P10 -> spine2 P10

P11 -> spine2 P11

P12 -> spine2 P12

P13 -> L1/P1

P14 -> L1/P2

P15 -> L1/P3

P16 -> L1/P4

P17 -> L1/P5

P18 -> L1/P6

P19 -> L1/P7

P20 -> L1/P8

P21 -> L1/P9

P22 -> L1/P10

P23 -> L1/P11

P24 -> L1/P12

SUBSYSTEM LEAF leaf2

P1 -> spine1 P13

P2 -> spine1 P14

P3 -> spine1 P15

P4 -> spine1 P16

P5 -> spine1 P17

P6 -> spine1 P18

P7 -> spine2 P19

P8 -> spine2 P20

P9 -> spine2 P21

P10 -> spine2 P22

P11 -> spine2 P23

P12 -> spine2 P24

P13 -> L2/P1

P14 -> L2/P2

P15 -> L2/P3

P16 -> L2/P4

P17 -> L2/P5

P18 -> L2/P6

P19 -> L2/P7

P20 -> L2/P8

P21 -> L2/P9

P22 -> L2/P10

P23 -> L2/P11

P24 -> L2/P12

SUBSYSTEM SPINE spine1

P30 -> leaf3 P6

P18 -> leaf2 P6

P6 -> leaf1 P6

P27 -> leaf3 P3

P15 -> leaf2 P3

P3 -> leaf1 P3

P31 -> leaf10 P6

P19 -> leaf11 P6

P7 -> leaf12 P6

P34 -> leaf10 P3

P22 -> leaf11 P3

P10 -> leaf12 P3

P43 -> leaf9 P6

P55 -> leaf8 P6

P67 -> leaf7 P6

P46 -> leaf9 P3

P58 -> leaf8 P3

P70 -> leaf7 P3

P42 -> leaf4 P6

P54 -> leaf5 P6

P66 -> leaf6 P6

P39 -> leaf4 P3

P51 -> leaf5 P3

P63 -> leaf6 P3

P29 -> leaf3 P5

P17 -> leaf2 P5

P5 -> leaf1 P5

P26 -> leaf3 P2

P14 -> leaf2 P2

P2 -> leaf1 P2

P32 -> leaf10 P5

P20 -> leaf11 P5

P8 -> leaf12 P5

P35 -> leaf10 P2

P23 -> leaf11 P2

P11 -> leaf12 P2

P44 -> leaf9 P5

P56 -> leaf8 P5

P68 -> leaf7 P5

P47 -> leaf9 P2

P59 -> leaf8 P2

P71 -> leaf7 P2

P41 -> leaf4 P5

P53 -> leaf5 P5

P65 -> leaf6 P5

P38 -> leaf4 P2

P50 -> leaf5 P2

P62 -> leaf6 P2

P28 -> leaf3 P4

P16 -> leaf2 P4

P4 -> leaf1 P4

P25 -> leaf3 P1

P13 -> leaf2 P1

P1 -> leaf1 P1

P33 -> leaf10 P4

P21 -> leaf11 P4

P9 -> leaf12 P4

P36 -> leaf10 P1

P24 -> leaf11 P1

P12 -> leaf12 P1

P45 -> leaf9 P4

P57 -> leaf8 P4

P69 -> leaf7 P4

P48 -> leaf9 P1

P60 -> leaf8 P1

P72 -> leaf7 P1

P40 -> leaf4 P4

P52 -> leaf5 P4

P64 -> leaf6 P4

P37 -> leaf4 P1

P49 -> leaf5 P1

P61 -> leaf6 P1

# Text boxes

Names List

Multiple NODE or SUBSYSTEM sections

SubNode Attributes

Multiple NODE or SUBSYSTEM sections

List of attributes for specific nodes in the hierarchy like:

Leaf1/U1=isBmaAgent=1

TOPSYSTEM

SYSTEM

SYSTEM

NODE or SUBSYSTEM  HEADER

List of Connections to

External CONNECTOR

Or

Other SUBSYS on same board.

Names List